## Slide 1: Clarifying the data rate requirement for wearable use case in RedCap SI
vivo, Guangdong Genius, Spreadtrum, Lenovo, Motorola Mobility, Xiaomi, Samsung, Apple, TCL, Panasonic, Sharp, OPPO, Convida Wireless, Quectel, Sony, Qualcomm
3GPP TSG RAN Meeting #88e RP-201223(revision from RP-200946)
Electronic Meeting, June 29 - July 3, 2020
Agenda Item: 9.9.5
Document for: Discussion & Decision

## Slide 2: Background
RedCap SID as approved in RP-193238 has following requirements included in the justification section

## Slide 3: Wearables
The data rate requirement for wearables as captured in the current SID is about High-end wearables
  Reference bit-rate: 10~50Mbps in DL and 5Mbps in UL
  Peak bit-rate: 150Mbps in DL and 50Mbps in UL
    Same as LTE Cat-4 UE
From the market perspective, most of wearable use cases do not requires such high data rate, while the other factors including compact device sizes, long battery life, low cost, etc, are more demanded.
  Including most of smart watches, rings, ehealth, medical monitoring, etc…
The data rate requirement for Low-end wearables
  Reference bit-rate: 5Mbps in DL and 2Mbps UL
  Peak bit-rate: up to 10Mbps in DL and 5Mbps in UL
    Same as LTE Cat-1bis UE
It has been discussed to add low-end wearables as one of the RedCap requirement in RAN1#101e
  Large majority of companies (~20) support the addition
  Some companies commented it is not part of the SID justification, so should be decided in RAN plenary

## Slide 4: Proposal
To update the SID justification section for wearables as the following
  Wearables: For High-end wearables, reference bitrate for smart wearable application can be 10-50 Mbps in DL and minimum 5 Mbps in UL and peak bit rate of the device higher, 150 Mbps for downlink and 50 Mbps for uplink. For Low-end wearables, reference bitrate can be 5Mbps in DL and 2Mbps in UL and peak bit rate of the device higher, 10Mbps for DL and 5Mbps for UL. Battery of the device should last multiple days (up to 1-2 weeks).