## Slide 1: On Coverage Recovery Study of R17 RedCap SID
Apple, OPPO, vivo, […]
3GPP TSG RAN Meeting #88e
Electronic Meeting, June 29 – July 3, 2020
RP-201224

## Slide 2: Background (1/2)
New SID on Support of Reduced Capability NR Devices was approved at RP-193238. Wearable use case was listed as one of three use cases i.e. industrial wireless sensors, video surveillance, wearables.
It was also explicitly emphasized in justification section of SID that smaller form factor is a common characteristic of the use case:
  “Finally, wearables use case includes smart watches, rings, eHealth related devices, and medical monitoring devices etc. One characteristic for the use case is that the device is small in size”

## Slide 3: Background (2/2)
The smaller form factor of wearable devices leads to lower antenna efficiency, thereby lower antenna gain impacting coverage of both UL and DL channels.
However, in the working group discussions, there was ambiguity on whether antenna gain loss due to small form factor can be modeled due to the following text in the objective section of the SID:

## Slide 4: Proposal
Update the SID Objective section for coverage recovery study as the following:
  Study functionality that will enable the performance degradation of such complexity reduction to be mitigated or limited, including [RAN1]:
    Coverage recovery to compensate for potential coverage reduction due to the device complexity reduction or smaller form factors.