## Slide 1: WID Revision Proposal: Increase Max DL TBS for LTE-M
Source: Sierra Wireless, Ericsson, Sony, Verizon, Telstra, AT&T, Nokia, Nordic Semiconductor, Telefonica, Telus ,KT, Orange, Rogers
RP-201233
(revision of RP-201157)

## Slide 2: Background/History
LPWA DL Speed Improvement History
    LTE-M HD-FDD CAT-M1:
        Rel 13 TBS 1000 300 kbps
        Rel 14 Ack Bundling 588 kbps
        Rel 17 14 HARQ ~700 kbps
    NB-IOT:
        Rel 13 NB1 28 kbps
        Rel 14 NB2 2 HARQs + TBS 1352 127 kbps
        Rel 17 16 QAM + TBS ~2600 ~250 kbps
Increase DL TBS technique
    Can be optionally applied on top of Ack Bundling and 14 HARQ technique
    Improvement is ~proportional to TBS increase
      E.g. TBS 1000=>1736 will provide ~73.6% speed increase

## Slide 3: Motivation
Similar motivations as the Rel 17 NB-IOT 16 QAM feature
Market expansion
    Improve support for watches and wearables
    Support for high data rate music or small format video
    Improved firmware download
    Improved user experience e.g. quicker point-of-sale transactions
Improved spectral efficiency
Improved battery life (i.e. allows UE to go to a low power state quicker)
  Given the trend to deploy denser cells for NR, higher TBS can often be utilized
Improved differentiation between NB-IOT and LTE-M
    Note: NB-IOT release 17 will increase speed by ~2X
  Easy specification change (details on next page)
  Easy commercialization (details on next page)

## Slide 4: Specification and Commercialization
Minimal specification changes:
Only needed for CE mode A
Increase Max DL TBS from 1000 to 1736
Rel 13 RAN1 specification already supports DL TBS up to 1736
No changes needed to: DCI, TBS tables, or CQI tables
Add a new UE capability (similar to how UL TBS was increased) – no new UE category
Soft buffer size decided by RAN1
  Easy commercialization
    Some commercial CAT-M1 chipsets can support increased DL TBS with a firmware change – thus no market fragmentation
    Easy change to eNB scheduler

## Slide 5: WID Changes
Proposal to add the following new objective to the WID:
  Add a UE capability to support a maximum DL TBS of 1736 [LTE-MTC] [RAN1, RAN2]
    CE Mode A only
    Determine soft buffer size [RAN1]
    Capability signalling [RAN2]

## Slide 6: Thank you