## Slide 1: Completing the EN-DC FDD-TDD PC2
RP-201269
Ericsson

## Slide 2: Completing the WI
Two outstanding issues:
Baseline solution supported by all UEs indicating EN-DC PC2 for an FDD-TDD band combination?
Fall-back when EUTRA and NR duty cycles exceeded?

## Slide 3: The ”blind” scheme should be the baseline
because it
is Rel-15 EN-DC power control, can be implemented by a Rel-15 UE
  The total average nominal power can never exceed 23 dBm in line with all other HPUE solutions
  100% FDD duty cycle possible while transmitting on the TDD
can be tested according to the existing 38-101-3 Rel-15 conformance tests
  such as verification of TDD dropping, same principle as PC3
does not require CG coordination for full functionality
  tight coordination on TTI level not supported by inter-node signaling
is actually not blind... neither is an EN-DC PC3 Rel-15
but it requires setting a UE-specific PLTE < 23 dBm
  standard for EN-DC PC3 to make sure TDD is not dropped with LTE at full power, PLTE released if EN-DC is released due to impared FDD UL coverage

## Slide 4: The ”blind” scheme is standard Rel-15 power control
At EN-DC connection establishment, a UE receives the UE-specific PLTE and EN-DC P-Max (if configured) along with all other information for the SCG (TDD) needed for establishing the connection like the common U/D pattern(s). Regardless of EN-DC power class
  An EN-DC PC3 uses the power class and the EN-DC P-Max (if configured) to set the maximum total EN-DC power threshold as specified in 38.213 Rel-15: the threshold is ≤ 23 dBm
  An EN-DC PC2 would use the power class, the PLTE (set to < 23 dBm) the EN-DC P-Max (if configured), compute the maximum TDD UL duty cycle from the common U/D pattern to obtain the maximum total EN-DC power threshold as specified in 38.213 Rel-15: the threshold is > 23 dBm up to 26 dBm depending on PLTE and duty cycle
The only difference between PC3 and PC2. Where is the complication?

## Slide 5: Example
Set PLTE = 22 dBm (1 dB power reduction) and assume max TDD UL duty cycle 25% as computed from the common pattern(s)
EN-DC PC3:
  total EN-DC threshold: 23 dBm
  max TDD power with concurrent LTE at full power (PLTE): 16 dBm, risk of TDD dropping (more the 6 dB scaling), PLTE = 21 dBm would be safer
  max TDD power without concurrent LTE = EN-DC power = 23 dBm
EN-DC PC3 with NR PC2:
  total EN-DC threshold: 25 dBm
  max TDD power with concurrent LTE at full power (PLTE): 22 dBm, no TDD dropping
  max TDD power without concurrent LTE = EN-DC power = 25 dBm
PC2 yields 6 dB increase of the TDD power for concurrent transmissions
  uncertain additional benefit with added duty-cycle reporting (including “UE-based P-MPR”)
  gain reduced with increased TDD duty-cycle and PLTE (still below 23 dBm)

## Slide 6: Duty-cycle reporting/management an option
Duty-cycle reporting add-on to the ”blind” baseline if supported by the UE (i.e. optional with capability reporting)
  tighter CG coordination improves performance (proprietary)
In the example: the UE may be able to set the total EN-DC power threshold at 26 dBm if duty-cycles (EUTRA and NR) are within capability, but uncertain gain for the example in practive
If, on the other hand, the operator configures PLTE = 23 dBm (or absent), then the duty-cycle method can provide gains if supported
Duty-cycle reporting requires modified UE conformance tests, more work in RAN5

## Slide 7: Fallback when duty cycles exceeded
The ”blind” scheme does not need fallback to PC3 (23 dBm), can be the total EN-DC power threshold (25 dBm in the example)
  independent of duty cycles, can be 100% on the FDD as required in SAR testing
For duty-cycle reporting schemes, fall-back to PC3 is proposed
  then most likely still configure PLTE < 23 dBm to make sure TDD is not dropped in fallback
The baseline ”blind” scheme set the (minimum) fallback level when duty-cycle schemes are used as add-on
  Why fallback to 23 dBm when a PLTE < 23 dBm is configured? Would be a waste of power

## Slide 8: Can be applied to other MR-DC
The blind scheme readily applies for both NR-DC PC2 and TDD-TDD EN-DC PC2
  based on Rel-16 NR-DC and Rel-15 EN-DC power control

## Slide 9: Conclusion
The ”blind” scheme the Rel-16 baseline, mandatory for UEs indicating EN-DC PC2
It can be implemented by a Rel-15 UE without changes (release independence)
No need to study this standard EN-DC Rel-15 power control scheme for Rel-17, what is to be studied?
Fall-back to the EN-DC threshold as set by the baseline, fallback to PC3 (23 dBm) would be waste of power when PLTE < 23 dBm is configured
A proprietary UE-based P-MPR scheme with unspecified behaviour should not be the baseline, but instead an optional add-on to the baseline like the other duty-cycle reporting schemes
  a CR implementing this in R4-2007053 (RAN4#95), duty-cycle reporting optional with capability added on top of the baseline
  no delay completing the WI
  the optional duty-cycle schemes require additinal work in RAN5 (conformance tests)

## Slide 10: Annex: a note on P-MPR
P-MPR can always be used on each CG as required (no difference from EUTRA)
Applies to all EN-DC PC2 schemes
  The ”blind” scheme only sets a total EN-DC power threshold at which the SCG should be scaled according to 38.213 Rel-15
  The output power on each CG can be reduced as much as required, e.g. if triggered by proximity sensors
    The total EN-DC power threshold need not be modified by P-MPR