## Slide 1: Summary of email discussion [R17_IIOT_scope] on Release 17 IIoT scope
Nokia, Nokia Shanghai Bell (Moderator)
3GPP TSG RAN Meeting #88e RP-201311
Electronic Meeting, June 29 - July 3, 2020
Agenda Item: 9.10.5
Document for: Discussion & Decision

## Slide 2: Email discussion status
There were 3 types of comments received
  Companies suggesting relative large scope
  Companies suggesting smaller scope
  Companies not suggesting to do anything
The moderator is proposing to aim for small scope approach, noting that it is an existing Release 17 objective, with details only deferred for later. The intention is not to aim for full feature parity (between unlicensed and lisenced) but focus on limited set of issues known from earlier Release 16 discussions already

## Slide 3: Proposed objective 2
2. Identify potential enhancements to ensure Release 16 feature compatibility with unlicensed band URLLC/IIoT operation in controlled environment Support for shared spectrum operation in controlled environment addressing the following [RAN1, RAN2]:
Ensure Rel-16 URLLC/IIOT feature parity between operation in licensed and unlicensed spectrum, covering at least
Support simultaneous configuration of multiple HARQ CBs with different priorities and new CBs introduced in R-16 NR-U
Support of NR-U features with DCI formats 0_2 and 1_2
Harmonizing configured-grant and SPS operation in NR-U and URLLC to ensure that multiple uplink CG and DL SPS configurations introduced in R-16 for IIoT can also work in unlicensed spectrum
Necessary adjustment for TDRA table (see next slide)
RP-XXXXX

## Slide 4: Proposed objective 2: TDRA table
One possible compromise here would be to limit the potential TDRA table enhancements for DCI formats 0_1 and 0_2 in a way, that for a single entry of the configured TDRA tables only either Feature A (Multislot PUSCH, from NR-U) or Feature B (PUSCH repetition, from URLLC) can be dynamically indicated, but not the combination of Feature A and B with a single UL grant.
This would keep the effort low
RP-XXXXX

## Slide 5: Other issues
PDCP specification retained
SA2 related modification as agreed (keeping ”if any”)