## Slide 1: Motivation for new WID on UE EMC enhancement
--Xiaomi

## Slide 2: Background
During the RAN4#96-e, Xiaomi has submitted a discussion paper for UE EMC as extending current requirements to UE supporting different features. A WF (R4-2012575) was agreed on potential UE EMC requirement extensions. Detail can be seen in the justification.
It has been raised the concern of TU and proper WID for the discussion as currently the discussion is under Rel-15 maintenance agenda. Considering the above, a UE EMC WID is proposed.
General Requirement
Additional Requirement
Clause suffix | Variant
None | Single Carrier
A | Carrier Aggregation (CA)
B | Dual-Connectivity (DC)
C | Supplement Uplink (SUL)
D | UL MIMO
E | V2X
Only General requirement
Single carrier only
CA/DC considered
Other features
Consider:
Integrity of standard
Coverage of requirements for different UE features
EMC
RF

## Slide 3: Justification
Current RAN4 UE RF specifications have defined UE general requirement for single carrier case as well as additional requirements for terminals supporting extra features, i.e. Carrier Aggregation (CA)/Dual-Connectivity (DC)/Supplement Uplink (SUL)/UL MIMO and V2X. Specific suffixes have been used for the sub clauses in TS 36.101 for LTE, TS 38.101-1 for FR1, TS 38.101-2 for FR2 and TS 38.101-3 for interworking operation with other radios.
A terminal which supports the features needs to meet both the general requirements and the additional requirement applicable to the additional clause with suffix.
Current RAN4 UE EMC specifications TS 38.124(NR) and TS 36.124(E-UTRA) only specify general requirements as single carrier cases. The requirements for a terminal supporting different features are not considered in current UE EMC specifications.
The RAN5 conformance test specification TS 38.521-1/-2/-3/-4 has defined test configurations for each test within FR1, FR2, interworking operation and performance respectively. However, there is no test configuration for UE EMC requirements, resulting to no guidance of UE EMC test to the industry.
Current regulatory requirements as ETSI EN 301 489-52 in Europe and CCSA YD/T 2583.18 in China also lack of guidance on the testing of UE supporting different features. It is RAN4 responsibility to analyze and define these requirements to better understand the UE feature performance under certain EMC tests.

## Slide 4: Objectives
Core part:
To complete the UE EMC requirements, following are as the scope:
Consider potential additional EMC requirements for NR UE supporting different features as defined in TS 38.101-1/-2/-3:
  emission requirements.
  immunity requirements.
  Limit the features which have been finished before Rel-17 to be considered
Consider potential additional EMC requirements for LTE UE supporting different features as defined in TS 36.101.
  emission requirements.
  immunity requirements.
  Limit the features which have been finished before Rel-17 to be considered
Define receiver exclusion band for UE supporting different features
Investigate current 3GPP UE EMC radiated emission limit.
  -Whether current test frequency range is suitable, including the lower and upper test frequency range.

## Slide 5: Objectives
Performance part:
  Investigate how to establish the communication link for NR and LTE UEs with different features
    Possible deltaRIB to be considered.
    Possible MSD to be considered.
  Investigate the test configurations for NR and LTE UEs with different features
    Investigate whether current test configuration defined in RAN5 can be re-used in EMC tests.
    Investigate whether current OTA test configuration can be reused for radiated emission test.
    Investigate whether regulations have already defined test configurations and if these regulations can be reused.