## Slide 1: Discussion on support for broadcast in Rel-17 MBS
Huawei, HiSilicon
3GPP TSG-RAN Meeting #89e RP-201871
Electronic Meeting, September 14 - 18, 2020
Agenda Item: 9.8.8

## Slide 2: Background
An LS has been sent from SA2 to RAN, RAN2 and RAN3 in S2-2006044/RP-201437, with the following information and request to RAN:
  SA2 is debating whether broadcast (i.e. without the network’s awareness about UEs receiving broadcast contents and for other use cases than the ones excluded already for Rel-17) should be further down-scoped in Rel-17 for remaining broadcast requirement in the SID. Some companies have provided solutions on broadcast (which are documented in the TR). SA2 would like to ask SA, RAN, RAN2 and RAN3 for feedback on broadcast support in Rel-17.

## Slide 3: Broadcast in RAN WID and SA2 SID
RAN Rel-17 NR MBS WIDs in RP-193248 (December 2019) and RP-201038 (June 2020) both include:
  Specify RAN basic functions for broadcast/multicast for UEs in RRC_CONNECTED state [RAN1, RAN2, RAN3]:
  Specify RAN basic functions for broadcast/multicast for UEs in RRC_IDLE/ RRC_INACTIVE states [RAN2, RAN1]:
NR Broadcast was included in S2-1901392 (Jan. 2019) from the beginning, and stays in the latest SA2 SID S2-2001858 (Feb. 2020), regardless of the addition/removal of Objective B in between these two versions:
  The goal of this Study Item is to identify and evaluate potential enhancements to the 5G system architecture to provide multicast-broadcast services which might be used for different vertical businesses.
  Define the framework, including the functional split between (R)AN and CN, to support multicast/broadcast services
Observation 1：NR Broadcast is in the scope of RAN Rel-17 NR MBS WID and SA2 Rel-17 MBS SID from the beginning

## Slide 4: Broadcast Use Cases
Observation 2: From moderator summary of RAN Rel-17 NR MBS email discussion (RP-191859), 22 out of 31 companies mentioned broadcast in use case discussion. The use cases under discussion included, but were not limited to:
  public safety messages (e.g. warning, emergency info/news) that need to be broadcast to all users which may not be within any group.
  critical V2X messages (e.g. car crash info) that need to be broadcast to all vehicles in proximity even though they are not within a group.
Observation 3: Group or subscription information from application layer may not be available to the 3GPP networks, in which case broadcast-based solutions in 3GPP networks have to be applied. This has been observed also from in LTE SC-PTM.

## Slide 5: Proposals
Proposal 1: The scope of Rel-17 NR MBS WID remains as it is (i.e. NR broadcast is included), and no further down-scoping or prioritization is needed.
Proposal 2: Inform SA2 about RAN decision with a reply LS (draft in RP-201870).