## Slide 1: Clarification of synchronization aspect for inter-cell multi-TRP in Rel-17 FeMIMO WI
Futurewei
RAN 89e
2020/09/14 - 2020/09/18
RP-201895
Agenda Item: 9.8.1
Document for: Discussion and Decision

## Slide 2: FeMIMO objective
R17 FeMIMO WID RP-193133
Enhancement on the support for multi-TRP deployment, targeting both FR1 and FR2:
  Identify and specify features to improve reliability and robustness for channels other than PDSCH (that is, PDCCH, PUSCH, and PUCCH) using multi-TRP and/or multi-panel, with Rel.16 reliability features as the baseline
  Identify and specify QCL/TCI-related enhancements to enable inter-cell multi-TRP operations, assuming multi-DCI based multi-PDSCH reception
  …

## Slide 3: Scenarios for R17 Inter-cell Multi-TRP
In Rel-16 eMIMO WI, RAN4 defined test set-up for multi-TRP (intra-cell) with
  Timing offset among multi-panel/TRP
    FR1 FDD with 15KHz
      Positive timing offset: 2us
      Negative timing offset: -0.5us
    FR1 TDD with 30KHz
      Positive timing offset : 1us
      Negative timing offset: -0.25us
Therefore, for inter-cell multi-TRP in Rel-17, the following 3 factors should be considered:
  Propagation delay difference is at least similar to that of Rel-16; in addition,
  Synchronization offset between multiple cells; and
    Note that inter-cell synchronization accuracy is up to 3us (TDD only) per RAN4 requirements
  Backhaul between the cells can be non-ideal with certain amount of delay
    This requires separate uplink transmissions to multiple TRPs of different cells
In RAN1 #102-e, some companies argued that synchronization and timing aspects for inter-cell multi-TRP are out of scope while others think it is a natural part of the practical scenarios

## Slide 4: Proposal
To proceed Rel-17 inter-cell multi-TRP work, there are 2 alternatives:
  Alt. 1: Only consider factor A, same as in the case of intra-cell
    The applicable scenarios will be very limited: very tightly synchronized cells with very fast backhaul and small cell sizes.
  Alt. 2: Consider all factors A, B, and C
    Applicable to more practical scenarios
RAN Plenary to determine between Alt. 1 and Alt. 2.