## Slide 1: 3GPP TSG RAN Meeting #90e RP-202511 Online Meeting, Dec. 2020
Title: FR2 CA fallback behaviour: Achieving consistency across WGs
Source: Qualcomm Incorporated

## Slide 2: Chronology
Original fallback behavior and signaling:
  It is mandatory for a UE to be able to fallback to lower order CA bandwidth class configuration within a fallback group
  Example of fallbacks for each sub-block of a 4+3 (H-I) configuration:
June 2018: Original fallback behavior and signalling, consistency across WGs
Aug 2019: Single CC fallback behavior agreed in RAN4.
Single CC fallback CR endorsed in RAN4
RAN88: Dedicated signaling not available for this behavior
RAN89: Core requirement change for all UEs proposed: Reduced fallback behavior
How to resolve??
3
2
1
2
1
RAN2 technically endorses CRs for signaling of new behavior
NBC = Non backward compatible
Requires dedicated signaling to prevent NBC signaling change. LS sent to RAN2
Dec 2018: FR2 Rel-15 complete in RAN4

## Slide 3: 3 Options to resolve conflict introduced in RAN4:
There are now 2 types of CA fallback behavior to reconcile in 3GPP
  Original fallback behavior
  Reduced fallback behavior proposal from RAN89 (as potentially agreeable replacement of single CC fallback behavior)
2 types of fallback behavior to reconcile
Option 1:
Retain original fallback behavior for all UEs
Option 2:
Adopt reduced fallback requirement for all UEs
Option 3:
Retain both types of fallback behavior requirements as capability
Y
N
Dedicated
reconsideration?
signaling available on

## Slide 4: Option 1 Detail
Retain original fallback behavior for ALL UEs, no signalling change
  Reverse RAN4 agreement that caused NBC change in RAN2
    Ex: Remove yellow highlighted sentence from RAN4 spec
    Standard returns to consistency
  UEs retain freedom to not declare support for any CA configuration
  Core requirement change for all UEs can be avoided, but testing reduction possible

## Slide 5: Option 2 Detail
Adopt reduced fallback requirement for ALL UEs, no signalling change
  Places burden of change on legacy UEs:
    A legacy UE that supports say, a 4+3 CA config. must now explicitly list out 14 additional fallback combinations to convey same information as before (4+2, 4+1, 4+0, 3+3, 3+2, 3+1, 3+0, 2+3, 2+2, 2+1, 2+0, 1+3, 1+2, 1+1)
    previously it was implicit that the UE meets RAN4 specifications in all fallback configurations listed above
  Sets a precedent for undermining RAN4 requirements:
    RAN4 requirements can become optional without RAN4 consensus
  Need to precisely define reduced fallback behavior in RAN4
  Need to make NBC RAN2 wording change to capture reduced fallback requirement
Option 2 is not viable because it sets undesirable precedents or employs undesirable methods (NBC) that compromise standards integrity

## Slide 6: Option 3 Detail
Retain both types of fallback behavior requirements for UEs to choose
  For standards consistency across WGs:
    New signaling is required for UEs that support reduced fallback behavior
      (see Option 2 detail for motivation)
      Technically endorsed RAN2 CR as a starting point?
    Original signaling shall be retained for UEs with original fallback behavior
  Need to precisely define reduced fallback behavior:
    Must include explicit list of RAN4 requirements that will not be supported by UE in fallback configurations (no ‘blank check’ on requirement exemptions)

## Slide 7: Options to resolve FR2 UE CA fallback behavior problem (while preserving 3GPP Standards Integrity)
 | Option 1: Retain original fallback behavior (Discard reduced fallback) | Option 3: Retain both types of fallback behavior requirements
RAN2 impact | None | New signaling is required for UEs that exhibit reduced fallback behavior. Original signaling retained for UEs with original fallback behavior
RAN4 impact | Remove statement in clause 4.2 of TS38.101-x that introduced conflict due to NBC nature of change: A terminal which supports CA or DC configurations, which include FR2 intra-band CA …. but can directly fall back to a single FR2 carrier. Deactivating carriers within the CA or DC combination is still possible. | For UEs that declare reduced fallback behavior: Explicit list of RAN4 requirement exemptions must be documented in spec

## Slide 8: WF
(reserved)