## Slide 1: WF on FR2 fallback
Apple
3GPP TSG RAN Meeting #90e RP-202556
Electronic Meeting, 7-11 December, 2020
Agenda Item: 14
Document for: Endorsement

## Slide 2: Summary of the initial round discussion
Option 1: relaxation for identified DL and UL requirements with signaling
Option 2: relaxation for identified DL and UL requirements without signaling
Option 3: relaxation only for identified DL requirements without signaling, no relaxation for UL requirements
Option 4: relaxation only for identified DL requirements with signaling, no relaxation for UL requirements
Option 5: No relaxation for both DL and UL requirements, with which RAN4 agreements are to be reverted
Some observations based on the 1st round discussion:
  Observation 1: option 4 and 5 are more popular than the others
  Observation 2: companies generally have less negative opinion on the option 4
  Observation 3: On signalling, companies’ views are diverse, but the related technical concerns may not be contradicted to each other.
    Concerning to introduce signalling includes no clear NW behaviour impact is identified
    Differentiating UE capability and performance is the main motivation to introduce the signalling.
  Observation 4: Majority prefers not to considering UL requirements exempt

## Slide 3: FR2 fallback related general agreements and assumptions
UE must support being configured with all the fallback band combinations and NW is not restricted to configure any fallback
The UE shall comply to all regulatory requirements for all supported band combinations, i.e. including for all fallback band combinations.
The qualified fallback band combinations, which can be allowed to comply with different set of identified requirements, should fulfill both of the following conditions
  consist of multiple sub-blocks
  have at least one sub-block comprising a contiguous CA combination (i.e. a letter B, C, D, …).

## Slide 4: WF on FR2 fallback related requirements
UE shall meet all UL requirements without exemption for all fallbacks.
UE shall meet all DL out-of-gap requirements for all fallbacks.
In relation to DL in-gap ACS and blocking, introduce per-UE capability IE xxx-FR2 in TS38.306.
  If IE xxx-FR2 is not present or set to be supported, the UE shall meet the UE RF requirements in clauses 7.5A, 7.5D, 7.6A, 7.6D in TS38.101-2 and 7.5A, 7.5B, 7.6A, 7.6B in TS38.101-3 for all combinations.
  If IE xxx-FR2 is set not to be supported, for each supported FR2 intra-band CA configuration with multiple sub-blocks, where at least one of the sub-blocks consists of a contiguous CA configuration, in-gap UE RF requirements of the highest order CA configuration in clauses 7.5A, 7.5D, 7.6A, 7.6D in TS38.101-2 and 7.5A, 7.5B, 7.6A, 7.6B in TS38.101-3 apply also to qualified fallback CA configurations with the same number of sub-blocks, where at least one of the sub-blocks consists of a contiguous CA combination.
The agreement on FR2 fallback shouldn’t be considered as the precedent to generally introduce capability signaling to make the existing RAN4 requirements optional. Instead, existing RAN4 requirements shall not be made optional by introducing capability signaling without consideration of all WGs impacts by change

## Slide 5: Implementation of the WF in specification
The following company CRs can be agreed at RAN #90:
  CR 0311 to 38.101-2 v15.11.0 (RP-20xxxx)
  CR 0312 to 38.101-2 v16.5.0 (RP-20xxxx)
  CR 0430 to 38.101-3 v15.11.0 (RP-20xxxx)
  CR 0431 to 38.101-3 v16.5.0 (RP-20xxxx)
  CR xxxx to 38.306 v15.11.0 (RP-20xxxx)
  CR xxxx to 38.306 v16.2.0 (RP-20xxxx)