## Slide 1: China Telecom,CATT
Motivation for New WI on coordination between LTE and NR in overlapping spectrum
3GPP TSG RAN Meeting #90 RP-202594
Dec 7 - 11, 2020
Agenda Item: 9.1.3
Document for: Discussion

## Slide 2: Background
In 4G era, some low-band spectrums, such as 1.8GHz, as the coverage layer was deployed in urban area while a second carrier (e.g., 2.1GHz) as capacity layer was deployed in the region with high capacity requirements. Since the downlink/uplink load of LTE cell are still high, it is hard to reframing the low-band spectrum in hotspot region to NR in short-term.
In 5G initial deployment phase, operators mostly deployed mid-band and high-band TDD spectrum which offer fantastic capacity but less coverage than the FDD bands traditionally used for 4G in dense urban region.
In order to achieve continuous NR coverage for 5G SA network, low-band 5G in FDD spectrum will be introduced in 5G network to rapidly extend coverage without requiring new sites.
Given that some low-band FDD spectrum(e.g., n1) can support up to 50MHz bandwidth in Rel-16, they can provide a fantastic capacity and coverage for low-capacity region.
Co-channel interference
NR Band | SCS kHz | 5 MHz | 10 MHz | 15 MHz | 20MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz
n1 | 15 | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes
 | 30 |  | Yes | Yes | Yes | Yes | Yes | Yes | Yes
 | 60 |  | Yes | Yes | Yes | Yes | Yes | Yes | Yes
n2 | 15 | Yes | Yes | Yes | Yes |  |  |  | 
 | 30 |  | Yes | Yes | Yes |  |  |  | 
 | 60 |  | Yes | Yes | Yes |  |  |  | 
n3 | 15 | Yes | Yes | Yes | Yes | Yes | Yes | Yes | 
 | 30 |  | Yes | Yes | Yes | Yes | Yes | Yes | 
 | 60 |  | Yes | Yes | Yes | Yes | Yes | Yes | 
The interference coordination/migration between LTE and NR shall be considered in Rel-17

## Slide 3: Scenario Introduction(1/2)
Scenario 1: the existing LTE 2.1GHz hotspot sites are upgraded to support DSS function which delivered both 4G and 5G service while more 2.1GHz NR sites without DSS function are built to provide continuous coverage for NR.
20MHz DSS
20MHz DSS
20MHz DSS
40MHz
clear NR
case1
case2

## Slide 4: Scenario Introduction(2/2)
Scenario2: LTE FDD and NR FDD are deployed in adjacent region
Outdoor Scenario: some low-band spectrums as 4G capacity layer were deployed in hotspot region while NR FDD spectrum can be deployed in adjacent region to achieve NR continuous coverage
Indoor Scenario: NR TDD(e.g., n77/n78) , due to its propagation characteristics, has difficulties in offering adequate coverage especially in some indoor scenarios. In order to improve the indoor coverage for NR, the low-band NR spectrum was introduced in DAS. The outdoor was also deployed by LTE FDD with low-band spectrum.

## Slide 5: Lab Test Results
Without any resource coordination and CRS migration, the downlink throughput of NR significantly decrease

## Slide 6: LTE-NR coexistence discussion in Rel-15
RAN1 already discussed on LTE-NR coexistence in Rel-15 and LS have been sent to RAN3 to support this feature in R1-1715041/R3-173397 as below:
RAN3 specified the feature only for the following two scenarios in Rel-15:
1)Coordination between eNB and en-gNB
2)Coordination between gNB and ng-eNB
LTE-NR coexistence coordination between eNB and gNB is not supported in Rel-15

## Slide 7: Discussion in Rel-17
A subset of this topic i.e. PRACH resource coordination between gNB and eNB was ever discussed in Rel-17 SON/MDT topic and the conclusion was that it should be discussed in TEI17 as a separate topic.
Considering LTE-NR co-existence is a dependent feature which covers several aspects including reference and control signaling resource indication, resource coordination, PRACH configuration coordination, etc., it is better to have a dedicated WI for it.
Proposal: It is proposed to agree the WID in RP-202596 to support LTE-NR co-existence between eNB and gNB.

## Slide 8: Possible solutions to support LTE-NR coexistence
Some possible options to support LTE-NR coexistence feature between eNB and gNB are as below:
  Option 1: Coordination between eNB and gNB via core network.
  Option 2: eNB coordinates with neighbour gNBs via co-located gNB node.
  Option 3: Setup direct interface between gNB and eNB.
Since option 3 has too much impact to RAN3 architecture, we propose to focus on the first two options or only Option2.
No new interface between LTE and NR shall be introduced in this WI
Option2: eNB coordinates with neighbour gNBs via co-located gNB node

## Slide 9
THANK YOU .
Notes: 模板来自于 http://docer.wps.cn