## Slide 1: On Msg3 enhancement in Rel-17 NR coverage enhancement WI
ZTE, Sanechips, Nokia, Nokia Shanghai Bell, China Telecom, SoftBank, Thales, Sharp
3GPP TSG RAN Meeting #90e
Electronic Meeting, December 7-11, 2020
Agenda: 9.7.4
RP-202666

## Slide 2: 1. Background (1/3)
The following channels are identified as the potential bottleneck channels in FR1.
  • 1st priority
  ‐ PUSCH for eMBB (for FDD and TDD with DDDSU, DDDSUDDSUU and DDDDDDDSUU)
  ‐ PUSCH for VoIP (for FDD and TDD with DDDSU, DDDSUDDSUU)
  • 2nd priority
  ‐ PRACH format B4
  ‐ PUSCH of Msg.3
  ‐ PUCCH format 1
  ‐ PUCCH format 3 with 11bit
  ‐ PUCCH format 3 with 22bit
  ‐ Broadcast PDCCH
The following channels are identified as the potential bottleneck channels for Urban 28 GHz scenario.
• PUSCH eMBB (DDDSU and DDSU)
• PUSCH VoIP (DDDSU and DDSU)
• PUCCH F3 11bits
• PUCCH F3 22bits
• PRACH B4
• PUSCH of Msg3

## Slide 3: 1. Background (2/3)
There has been experience in LTE where coverage enhanced UEs and legacy LTE UEs are co-existing in the same network. During RAN1 discussion, companies especially operators have proposed several relevant scenarios for Msg3 enhancement.
• Heterogeneous network, where Rel-15/16 UEs can still access the network via Macro layer in the enlarged cell region.
• Outdoor gNB serves deep indoor UE, e.g, in Rural 700MHz/4GHz scenario.
• Isolated cell in the countryside.
• Increasing coverage or data rate of Msg3.
Enhance accessibility for Rel-17 UEs in deep indoor
Enlarge isolated cell coverage in countryside
NOTE: NR NTN may benefit from the NR coverage enhancement techniques studied for UL channels, conditioned on potential corresponding discussions in NR NTN WI.

## Slide 4: 1. Background (3/3)
Enhancements on Msg3 PUSCH repetition were studied from several aspects in RAN1.
Indication of the number of repetitions for Msg3 initial transmission and re-transmission
Repetition type
Feasibility and applicability of enhancements studied for PUSCH in RRC_CONNECTED state for Msg3 PUSCH initial and re-transmission
Inter-slot frequency hopping
Differentiation between enhanced UE and legacy UE

## Slide 5: 2. Proposal for Msg3 enhancement
Proposal: Support Msg3 PUSCH repetition in Rel-17 NR coverage enhancement work item.

## Slide 6: Thank you