## Slide 1: Way forward on NR Coverage Enhancements
MediaTek Inc.
3GPP TSG RAN#90E RP-202694
December 2020 Agenda Item 9.1.1

## Slide 2: Introduction
SI declared complete with the following outcome
  Identification of the bottleneck channels for the scenarios and deployments based on link budget (both FR1 and FR2).
  Potential enhancement solutions for the bottleneck channels based on analysis and simulations.
Additionally
  Prioritization of some scenarios and/or channels for potential enhancements.
  Documentation of the observations for the potential solutions in TR.
  Recommendation of some potential enhancement solutions.

## Slide 3: WI Scope considerations General
Channels to be enhanced that are:
  Identified as bottleneck channels in most or typical scenarios
  Prioritized (as 1st priority) with the potential enhancement solutions recommended by RAN1
Prioritize the bottleneck channels common to both FR1 and FR2
  A set of channels are identified for FR2@28GHz except for indoor scenarios Enhancements for these channels for FR2 may imply either a redesign of the system or problematic configurations i.e. to be addressed primarily by deployment
  Considering the work load and schedule, the common bottleneck channels need to be prioritized
Additionally, avoid WI/SI overlap

## Slide 4: Channels to be enhanced
PUSCH Enhancement
  PUSCH has been identified as the bottleneck channel in most scenarios (incl. FR1 and FR2). Potential solutions have been recommended in RAN1.
  Additionally, PUSCH Msg 3 enhancement can be included as part of PUSCH enhancement.
    Low-hanging fruit and beneficial for the coverage of the larger payload size of Msg 3 (72bits raised by RAN2).
  PUSCH enhancement should be generic and as such applicable to any scenario e.g. NTN, RedCap
    i.e. no other dedicated PUSCH enhancement for e.g. NTN, RedCap

## Slide 5: Considerations for other WI
PUCCH Format 3 with 11/22 bits for Enhancement
  Deprioritized in RAN1 (2nd priority).
  The coverage issue may also need some SLS evaluation for confirmation.
    The required uplink coverage should also be checked according to the coverage of the DL high rank transmission.
  For multi-TRP case, PUCCH reliability issue can be left for FeMIMO study

## Slide 6: Others
PRACH B4:
  Deprioritized for FR1 (2nd priority)
  Beneficial for FR2 but some other channels should also be enhanced as well to make the system work

## Slide 7: Summary
WI scope of coverage enhancement to consider
  RAN1 study outcome
  Commonality for FR1/FR2
  Work split between potential overlapping WIs
Proposed channels for enhancement under CovEnh WI:
  PUSCH (incl Msg3) as a generic enhancement i.e. implicitly applicable to any use cases (e.g. RedCap, NTN)
FR2-specific channel enhancement is not preferred
  Too many bottleneck channels identified
  I.e. resolve via deployment to avoid complete redesign