## Slide 1: View on scope of supporting NR from 52.6GHz to 71GHz
RP-202756
3GPP TSG RAN Meeting #90e December 7-11, 2020

## Slide 2: Background
SI on NR extension up to 71GHz:
  Successfully completed in RAN1 on Q4 2020 and
  is on track for completion in Q1-2021 in RAN4
A set of numerologies (subcarrier spacings, SCS) were identified for further consideration
Potential enhancements to physical layer signals and channels were also identified to support operation with higher phase noise and higher SCS
Both LBT mode and no-LBT mode are to be supported and baseline channel access mechanism has been identified

## Slide 3: SCS decisions from SI
120KHz supported, and one or two SCS supported out of 240/480/960kHz
  If one additional SCS supported, 480kHz or 960kHz
  If two additional SCS supported, any combinations (480+240), (960+240) or (480+960)
  NR should be designed with maximum FFT size of 4096 and maximum of 275 RBs per carrier;
Potential physical layer impacts for each numerology are identified as follows:
 | 120 | 240 | 480 | 960
Potential consideration of PTRS enhancement for CP-OFDM and DFT-s-OFDM, if needed. | X | X | X | 
SSB patterns, and CORESET#0 configuration |  | X | X | X
RO configuration |  | X | X | X
Timelines for scheduling, processing and HARQ |  | X | X | X
Potential enhancement to DM-RS, if needed |  | X | X | X
PDCCH monitoring |  | X | X | X
Potential consideration of ECP, if needed, depending on deployment scenarios |  |  |  | X
Potential updates to smallest time unit, Tc, used in specifications depending on supported maximum carrier BW |  |  |  | X

## Slide 4: Discussion on SCS selection
SCS selection is critical for the progress of the Work Item
  Most of the PHY signals and channels designs will depend on the SCS assumed
    It is preferred to determine the SCS choices early to avoid throttling other designs and decisions
From the identified PHY impacts, the effort to introduce each new numerology is similar
From performance evaluation of different numerologies in the study item phase
  All numerologies have similar performance
    with smaller SCS supporting larger coverage and
    with higher SCS supporting higher peak rate
Considering that 120kHz SCS is agreed to be supported, the coverage limited use case is supported
  Considering one of 480kHz and 960kHz supported, additionally supporting 240kHz will only provide minor benefit, while unnecessarily complicating the design and implementation of the system
  To support higher peak rate use case, we believe 960kHz SCS is a better choice than 480kHz (supporting wider bandwidth and higher peak data rate with a single CC), however, we understand 480kHz can provide longer CP length, better fit for outdoor deployment
For SSB SCS, we should support same SSB SCS as data/control for easier implementation
  But for initial access, a single SCS should be assumed per band, and given the better coverage of 120kHz SCS, this is the preferred choice for initial access SSB SCS
  For PRACH, same set of SCS as control and data can be supported

## Slide 5: Proposal
Initial access signals and channels:
  120kHz and 240kHz (SSB/PBCH block numerology, i.e., legacy Rel-15 FR2) + 120kHz SIBs
Control/data channels:
  120kHz and 960kHz (higher SCSs are optionally supported by UEs)
  Additional support of 480kHz can be considered esp. suited for outdoor scenarios
Definition of SSB/PBCH block for new SCS(s) for cases other than initial access, e.g., mobility, should follow Rel-15 design to the extent possible
PRACH should support same numerologies as control/data channels