## Slide 1: Support for Public Safety Needs in Release 17
Eshwar Pittampalli, FirstNet
Supporting Companies
FirstNet, AT&T, NTIA , UK Home Office, MINISTERE DE L'INTERIEUR FRANÇAIS, SyncTechno Inc., Suomen Erillisverkot Oy, A.S.T.R.I.D. S.A., Norwegian Communications Authority, Softil, The Netherlands Police, BMWi

## Slide 2: Outline
As previously presented in SP-191116, the public safety community identified the following as High Priority Topics to support public safety needs:
  System enhancement for Proximity based Services in 5GS (5G_ProSe)
  Architectural enhancements for 5G multicast-broadcast services (5MBS)
  Enhancement to the 5GC LoCation Services-Phase 2 (eLCS_ph2)
  Integration of Satellite in 5G Systems (5GSAT_ARCH)
These areas were also identified as high priority for other verticals such maritime safety and maritime commercial usage.
As SA2 concludes study items and starts discussion of the related work items, it is important to highlight some of the key features within these work items that are important to be included in Release 17 for Public Safety

## Slide 3: System enhancement for Proximity based Services in 5GS (5G_ProSe)
ProSe Release 17 is expected to deliver a solution that enables public safety services to migrate to 5G.
ProSe Release 17 should address:
  Support of one-to-many direct communication including out-of-coverage
  Support of one-to-one direct communication including out-of-coverage
  Support of UE-to-Network Relay including:
    Service continuity
    QoS
  Support of direct discovery including out-of-coverage
  Support of UE-to-UE relay mechanism

## Slide 4: Architectural enhancements for 5G multicast-broadcast services (5MBS)
At a minimum, 5MBS should support the following features:
  Multicast and broadcast communication service within 5G system, including:
    Multicast communication
    Broadcast communication
    QoS support for multicast and broadcast.
  Interworking with EPC/eMBMS for Public Safety.

## Slide 5: Enhancement to the 5GC LoCation Services-Phase 2 (eLCS_ph2)
eLCS_ph2 should support the MCS requirements as stated in TS 22.280 clause 7.8 and clause 7.9 for in-network and off-network scenarios:
  [R-7.8-001] An MCX UE shall be capable of transmitting its Location, if known, to other MCX UEs when operating off the network, subject to privacy restrictions.
  [R-7.8-002] An MCX UE shall be capable of providing a mechanism for obtaining the distance between the MCX UE and other MCX UEs within communication range.
  [R-7.8-003] The Off-Network MCX Service shall provide a means for an authorized MCX User to activate a one-time Location information report of a particular target MCX User within communication range.
  [R-7.9-001] MCX UEs operating off the network shall be capable of protecting the confidentiality of Location and identity information conveyed to or from other MCX UEs.
  [R-7.9-002] MCX UEs operating off the network shall be capable of authenticating the sender of messages carrying Location and identity information.

## Slide 6: Integration of Satellite in 5G Systems (5GSAT_ARCH)
5GSAT should support the following to meet Public Safety requirements:
  Mobility management
  QoS

## Slide 7: Summary
Ensure that the high priority topics identified by the Public Safety community are completed as part of Release 17
Ensure that identified features within these high priority topics will be included in Release 17 scope

## Slide 8: Back-up

## Slide 9: Support for Public Safety Needs Ref: SP-191116
Enhancements to 5G to support MCS identification for:
  Access Control
  Resource allocation
  Resource Retention
  Priority Treatment
Multicast Broadcast Services over 5G
Enhanced Location Services over 5G
IMS Core evolution to support 5G
5G Proximity Services (Including Multi-Hop Relay)
Integration of Satellite in 5G Systems
Extend Coverage
Availability
(Priority Treatment)
MCS Enablers
MC application architecture support in 5G
MC service enhancements and continued evolution
MCS Services