## Slide 1: Motivation for New WID on NR SL Relay
OPPO

## Slide 2: Sidelink Relay Use Cases
UE-to-Network Relay: Address the requirement for network coverage extension
UE-to-UE Relay: Address the requirement for UE/Sidelink coverage extension
Applicable Scenarios include
  V2X
  Public Safety
  Commercial

## Slide 3: NR Sidelink Relay Stage-1 requirement
In 22.261, KPI for UE-to-Network Relay has been provided
  InHome Scenario
  Factory Sensors
  Smart Metering
  Containers
  Freight Wagons
  Public Safety
  Wearables
Scenario | Max. data rate (DL) | Max. data rate (UL) | End-to-end latency (note 7) | Area traffic capacity (DL) | Area traffic capacity (UL) | Area user density | Area | Range of a single hop (note 8) | Estimated number of hops
InHome Scenario (note 1) | 1 Gbit/s | 500 Mbit/s | 10 ms | 5 Gbit/s/ home | 2 Gbit/s /home | 50 devices /house | 10 m x 10m – 3 floors | 10 m indoor | 2 to 3
Factory Sensors (note 2) | 100 kbit/s | 5 Mbit/s | 50 ms to 1 s | 1 Gbit/s /factory | 50 Gbit/s /factory | 10000 devices /factory | 100 m x 100 m | 30 m indoor / metallic | 2 to 3
Smart Metering (note 3) | 100 bytes / 15 mins | 100 bytes / 15 mins | 10 s | 200 x 100 bytes / 15 mins /hectare | 200 x 100 bytes / 15 mins /hectare | 200 devices /hectare | 100 m x 100 m | > 100 m indoor / deep indoor | 2 to 5
Containers (note 4) | 100 bytes / 15 mins | 100 bytes / 15 mins | 10 s | 15000 x 100 bytes / 15 mins /ship | 15000 x 100 bytes / 15 mins /ship | 15000 containers /ship | 400 m x 60 m x 40 m | > 100 m indoor / outdoor / metallic | 3 to 9
Freight Wagons | 100 bytes / 15 mins | 100 bytes / 15 mins | 10 s | 200 x 100 bytes / 15 mins /train | 200 x 100 bytes / 15 mins /train | 120 wagons /train | 1 km | > 100 m outdoor / tunnel | 10 to 15
Public Safety (note 5) | 12 Mbit/s | 12 Mbit/s | 30 ms | 20 Mbit/s /building | 40 Mbit/s /building | 30 devices /building | 100 m x 100 m – 3 floors | > 50 m indoor (floor or stairwell) | 2 to 4
Wearables (note 6) | 10 Mbit/s | 10 Mbit/s | 10 ms | 20 Mbit/s per 100 m2 | 20 Mbit/s per 100 m2 | 10 wearables per 100 m2 | 10 m x 10 m | 10 m indoor / outdoor | 1 to 2

## Slide 4: NR SL Relay Stage-2 conclusion: U2N Relay
 | RAN2 |  | SA2 | 
 | L2 | L3 | L2 | L3
Discovery | Studied |  | Model A, Model B | 
Relay (re-)selection | Studied |  | The radio aspects up to RAN2 | 
Authorization | Up to RAN3 |  | Coordinate with SA3 | 
Protocol Stack | Studied | Up to SA2 | Annex A | Studied (Sol#6, Sol#23)
QoS | gNB Implementation | Up to SA2 | Up to RAN2 | Studied (Sol#24, option-2 of Sol#25)
Security | Studied (secured by PDCP) | Up to SA2/SA3 | Up to RAN2 and SA3 | Studied (Sol#23), up to SA3
Service Continuity | Studied | Up to SA2 | Up to RAN2 | Studied (Sol#26)
CP | Studied PC5-S up to SA2 | Up to SA2 | (Sol#7) Up to RAN2 | Studied (Sol#6, Sol#23)
Red part is the one with key/major specification effort.

## Slide 5: NR SL Relay Stage-2 conclusion: U2N Relay
UE-to-Network Relay extensively studied in RAN2/SA2
No show-stopper for both L2/3 architecture, from both SA2 and RAN2 perspective
Complexity/Spec-effort wise: L2 is more on RAN2, while L3 is more on SA2
Quite some support on both L2/3
=> Both L2/3 U2N are feasible for R17 WI

## Slide 6: NR SL Relay Stage-2 conclusion: U2U Relay
 | RAN2 |  | SA2 (No conclusion yet) | 
 | L2 | L3 | L2 | L3
Discovery | Studied |  | Model A, Model B | 
Relay (re-)selection | Studied |  | Studied (Sol#8, Sol#50) | 
Authorization | No RAN2 impact |  |  | 
Protocol Stack | Studied | Up to SA2 | Studied (Sol#9) | Studied (Sol#10, Sol#32, Sol#49)
QoS | No AS impact | Up to SA2 | Studied (Sol#31, Concluded) | Studied (Sol#31)
Security | Studied (secured by PDCP) | Up to SA2 | Up to RAN2 and SA3 | Up to SA3
Service Continuity | N.A. | N.A. | N.A. | N.A.
CP | Dependent on PC5-S design by SA2 (have not finished before last RAN2 meeting in SI) | Up to SA2 | Studied (Sol#9) | Studied (Sol#8, Concluded)
Red part is the one with key/major specification effort.

## Slide 7: NR SL Relay Stage-2 conclusion: U2U Relay
UE-to-UE Relay studied in RAN2/SA2, but not sufficiently
No show-stopper for both L2/3 architecture, from both SA2 and RAN2 perspective
Currently, L2 solution seems risky for both RAN2 and SA2,
  Considering the CP procedure design for PC5-S is finished quite late at SA2
  L2 solution also has impact on SA2 side
Less interest from vendors
=> Although both L2/3 U2U Relay is feasible, L2 U2U Relay is risky on spec effort

## Slide 8: Options on the table
Option | L2 U2N | L3 U2N | L2 U2U | L3 U2U | 
1 |  | X |  | X | Solution by L3 proponent
2 | X |  | X |  | Solution by L2 proponent
3 | X | X | ? | ? | U2N is of joint interest by commercial and public-safety, while U2U is more of interest by public safety use case; At RAN side, the spec impact due to L3 solution (discovery, (re)selection as the common part of L2/3 solutions) is a subset of spec impact due to L2 solution, i.e., main effort is for L2 solution L2 + L3 U2N is of a compromise point The proposal on U2U has to consider both the resource / load restriction at WG level at R17, solution (a)symmetry for U2N and U2U
4 | X | X | X | X | Solution out of the capacity of WG in R17

## Slide 9: Rel-17 WI Objectives (1/4)
1. Specify mechanism(s) for Layer-3 (L3) Sidelink-based UE-to-Network Relay
  Relay discovery and (re)selection [RAN2, RAN4];
  Relay and Remote UE authorization [RAN3];
  [QoS management [RAN2];]
Layer-3 enablers are generally a subset of Layer-2 enablers;
Layer-3 mainly on discovery, relay (re)selection

## Slide 10: Rel-17 WI Objectives (2/4)
2. Specify mechanism(s) for Layer-2 (L2) Sidelink-based UE-to-Network Relay,
  Relay discovery and (re)selection [RAN2, RAN4];
  Relay and Remote UE authorization [RAN3];
  QoS management [RAN2];
  Service continuity [RAN2, RAN3];
  Adaptation layer design [RAN2];
  Control Plane procedure design, including RRC connection management, system information delivery, paging mechanism and access control for Remote UE [RAN2];
Layer-2 in addition has impact on service continuity, adaptation layer design for UP, and CP procedure (including RRC state control, SI delivery, paging)

## Slide 11: Rel-17 WI Objectives (3/4)
[3. Specify mechanism(s) for Layer-3 (L3) Sidelink-based UE-to-UE Relay
  Relay discovery and (re)selection [RAN2, RAN4];]
For U2U, we assume there is little delta part in terms of discovery and relay (re)selection from AS perspective, compared with the mechanism for U2N relay

## Slide 12: Rel-17 WI Objectives (3/4)
[4. Specify mechanism(s) for Layer-2 (L2) Sidelink-based UE-to-UE Relay
  Relay discovery and (re)selection [RAN2, RAN4];
  Adaptation layer design [RAN2];
  Control Plane procedure design, including connection management [RAN2]]
For U2U, we assume there is little delta part in terms of discovery and relay (re)selection from AS perspective, compared with the mechanism for U2N relay

## Slide 13: Rel-17 WI Objectives: NOTEs
NOTE 1: For L3 UE-to-Network Relay (Objective-1) and L2 UE-to-Network Relay (Objective-2), for bullet a) and b), RAN2 and RAN3 target at a common solution as captured in TR 38.836. For L3 UE-to-UE Relay (Objective-3) and L2 UE-to-UE Relay (Objective-4), for bullet a), RAN2 targets at a common solution as captured in TR 38.836.
NOTE 2: For L2 UE-to-Network Relay, it is assumed that the Remote UE has a single active connection towards gNB via only a single Relay UE at a given time in this release.
NOTE 3: Only NR Uu interface, i.e. gNB, and 5GC is considered, and it is limited to NR SA scenario in this release.
NOTE 4: For bullet d) above of UE-to-Network Relay, include both intra-gNB and inter-gNB cases, but deprioritize work specific to the mobility scenario of “between indirect (via a first Relay UE) and indirect (via a second Relay UE)” and the group mobility in this release.
Scenario simplification is necessary for a focused and manageable scope for R17, including topology, RAT and mobility scenario;