## Slide 1: new bands and bandwidth allocation for 5G terrestrial broadcast
RAN #91-e, March 16-26, 2021
A.I: 10.1.4

## Slide 2: Background
LTE based 5G terrestrial broadcast:
  Enables deployment of broadcast, downlink-only network.
  Introduced in Rel-14, evolved in Rel-16.
A clear target for deploying this technology is broadcast UHF spectrum
  Between ~470MHz - ~698MHz, depending on the region.
  Channelization is based on 6/7/8MHz.

## Slide 3: Enhancements for UHF spectrum
There are two main enhancements needed to enable operation in UHF:
  Bandwidth: 5GTB does not support 6/7/8MHz. Operating at 5MHz channel bandwidth wastes a large percentage of spectrum.
  Band definition: The UHF broadcast band is not defined as a 3GPP band.
We propose to close this gap with a short RAN4-led work item in Rel-17.

## Slide 4: Proposal
Start a short RAN4-led work item (RP-210127) with the following objectives:
  Introduce PMCH bandwidth of 6/7/8MHz [RAN1]
  Define UE / BS requirements for the new PMCH bandwidth [RAN4]
  Introduce band(s) supporting 6/7/8MHz in UHF broadcast spectrum [RAN4]

## Slide 5: FOLLOW the ebu
@EBU_HQ
www.ebu.ch, tech.ebu.ch
EBU UPDATE monthly newsletter
facebook.com/EBU.HQ
linkedin.com/company/ebu
instagram.com/ebu_hq/