## Slide 1
Agenda Item: 9.7.4
Source: Samsung
Title: Views on Multi-Cell PDSCH Scheduling via a Single DCI
Document for: Discussion and Decision
3GPP TSG RAN Meeting #91e
Electronic Meeting, March 16 - 26, 2021
RP-210292

## Slide 2: Overview
The WID on NR Dynamic spectrum sharing (DSS) includes
  Study, and if agreed specify PDCCH of P(S)Cell/SCell scheduling PDSCH on multiple cells using a single DCI
    The number of cells can be scheduled at once is limited to 2
    The increase in DCI size should be minimized
RAN1 completed the study on scheduling 2 PDSCHs on 2 cells using single DCI [R1-2102138]
General observations for a 2-cell scheduling DCI
  DCI overhead savings without penalty on throughput include (a) CRC, (b) fields for PUCCH transmission with HARQ-ACK (TPC command, slot indicator, resource indicator) and (c), the DAI field (for Type-2 HARQ-ACK codebook)
  Reducing a few bits from other fields has a direct negative impact on throughput (negative tradeoff)
  There was generally good alignment among companies in link-level simulation results - on average, use of one PDCCH/DCI to schedule 2 PDSCHs on 2 cells requires 1-2 fewer CCEs than use of two respective PDCCHs/DCIs

## Slide 3: Ideal Theoretical Throughout Gain from Single DCI
RAN1 evaluations assumed that all PDCCHs only schedule PDSCHs on two cells, all the time
  Best case scenario for one PDCCH/DCI scheduling PDSCH on two cells
  Unrealistic scenario because PDCCH is also used to schedule single-cell PDSCH, PUSCH, or for common control
Theoretical throughput/spectral efficiency gain is simple/transparent to compute using basic information theory and Shannon’s capacity formula (gain is proportional to BW savings)
  For cells with small contiguous BW, such as 10 MHz at 700 MHz bands, at most 1-2 UEs are scheduled with CA per slot on average
  A number of such (contiguous spectrum) cells per operator on sub-GHz bands is very small
  Saving 1-2 CCEs (6-12 RBs) for scheduling per pair of cells corresponds to BW savings per slot
    For scheduling cell of 20 MHz (100 RBs), gain is 6-12 (RBs) x (2 cell pairs) /(100 RBs/symbol x 14 symbols) = 0.85% - 1.7%
    For scheduling cell of 100 MHz (500 RBs), gain is 6-12 (RBs) x (2 cell pairs) /(500 RBs/symbol x 14 symbols) = 0.017% - 0.034%

## Slide 4: Actual Throughout Gain from Single DCI
For any CCE savings to translate to throughput gains, saved CCEs need to be possible to use for PDSCH; however, that is not possible when any of the following typical events also occurs in a CORESET
  PDCCH that schedules PDSCH for any other UE
  PDCCH that schedules PUSCH for any UE
  PDCCH transmission for common control
To circumvent the above limitations, reduced CORESET sizes (due to savings of 1-2 CCEs for scheduling PDSCH per cell-pair) were suggested; however, that is not realistic at least because a CORESET size cannot be dimensioned only for when one PDCCH schedules only 2 PDSCHs on 2 cells all the time
  Additional factors reversing any gain exist, such as padding/increasing size of UL DCI formats to maintain DCI format size budget
Conclusion on throughput
  Under ideal (and non-realistic) assumptions, maximum theoretical gains from a PDCCH scheduling 2 PDSCHs on 2 respective cells are negligible
  Actual gains from a PDCCH scheduling PDSCH on two cells are zero

## Slide 5: PDCCH Blocking
PDCCH blocking was another comparison metric between 2 PDCCHs vs. 1 PDCCH to schedule 2 PDSCHs
Given the average savings of 1-2 CCEs for scheduling 2 PDSCHs with 1 PDCCH (versus 2 PDCCHs), and that scheduling is at most on 2 cell pairs at sub-GHz, PDCCH blocking is fundamentally not an issue
Similar to throughput evaluations, several companies considered PDCCH blocking for scenarios not reflecting actual deployments, such as:
  Continuous PDSCH scheduling on at least 5, and typically more than 10, cell-pairs in every slot
  No other PDCCH in CORESET – e.g. no PDCCH for scheduling single-cell PDSCH or PUSCH, or for common control
  Use of only one CORESET (use of multiple CORESETs is mathematically guaranteed to lower blocking - also known by simulations)
  Blocking probabilities were already too high, both for using 1 PDCCH and 2 PDCCHs (for scheduling 2 PDSCHs)
  No consideration of the increase in PDCCH blocking probability due to requirements to increase UL DCI size in order to maintain the DCI format size budget when using a single DL DCI to schedule 2 DL cells
Conclusion on blocking: Reduction of PDCCH blocking from using 1 PDCCH to schedule 2 PDSCHs on a cell pair is practically zero and can occasionally, due to required padding of UL DCI, even be negative

## Slide 6: Conclusions
Using 1 PDCCH to schedule 2 PDSCHs on 2 cells offers marginal gain in theory and no gain in reality
Expected RAN1/RAN2 specification work can be substantial and include at least
  DCI format design that can involve practically every field in the DCI format
  Determination of maximum PDCCH candidates/non-overlapping CCEs per slot per scheduled cell (including when cells in a cell-pair have different SCS), PDCCH overbooking UE procedures, etc.
  HARQ-ACK codebook design
  Other aspects, such as indication of cell pairs (e.g. RRC or DCI-based), search space design, TB scheduling per cell or TB scheduling across two cells, etc.
Considering the absence of any benefit, that Rel-17 has already been extended, and that e-meetings are expected to continue at least for most of Rel-17, RANP should not endorse any further work on the topic
Proposal: WGs do not perform any further work in Rel-17 on the use of 1 PDCCH/DCI to schedule 2 PDSCHs on a respective pair of cells