## Slide 1
3GPPTSG RAN Meeting #91e RP-210311
Electronic Meeting, March 16 - 26, 2021
Agenda Item: 9.6.6
Document for: Discussion & Decision
WID scope for Rel-17 sidelink relay

## Slide 2
A Rel-17 Study Item of “Study on NR Sidelink Relay”has been carried out by 3GPP in RAN2, the study item covered enhancements and solutions necessary to support the UE-to-network Relay and UE-to-UE Relay
Mechanisms for L2 relay and L3 relay have been studied and identified by RAN2, striving for minimum specification impact. The standards impact of L2 relay is principally in RAN and the standards impact of L3 relay is principally in SA. In this study, both L2 based Relay architecture and L3 based Relay architecture have been found feasible [R2-2102060].
RAN2 has also studied direct discovery procedure, UE-to-Network Relay, and UE-to-UE Relay solutions.
Background

## Slide 3
L3 UE-to-Network relay architectures have the following characteristics:
  Have better performance in the scenario of Relay UE mobility than L2 group mobility;
  L3 has lower RAN specification impact;
    Proposal 1: L3 U2N should be considered as baseline for SL Relay WI.
The RAN2 SI concluded with the following recommendation:
  RAN2 recommends both L2 and L3 UE-to-Network and UE-to-UE Relay can proceed to normative work.
    Proposal 2: RAN to confirm that both L2 and L3 U2N SL Relay architecture are in WI scope.
    During RAN2 SI phase no typical important scenario of U2U SL Relay was identified and
    U2U SL Relay may need different designs from U2N SL Relay, e.g. Relay selection/reselection, establishment procedure and so on. Time unit is limited.
    Proposal 3: Assessment of work load should done before including U2U SL Relay in Release 17 WI scope.
    The SI focused on single hop SL Relay scenario. There was no stringent requirement to consider multi-hop L2 Relay scenario. Considering forward compatibility for multi-hop L2 Relay would require additional and redundant design on both Relay UE and Remote UE.
    In case multi-hop case is proven to be supported, extended design of single hop scenario can be firstly considered.
    Proposal 4: Forward compatibility for multi-hop L2 relay support is not considered in this release.
  Scope of the new WID