## Slide 1
3GPP TSG RAN Meeting #91e RP-210320
Electronic Meeting, Mar. 22-26, 2021
Source: vivo
Document for: Discussion & Decision
Agenda Item: 9.7.27
Performance issues with supporting 2Rx
for wearables in FR1

## Slide 2
  Supporting 1Rx is crucial to enable wearable use cases with form factor limitations.
      Most of LTE based smart watches in the market are equipped with 1Rx due to implementation challenges, although the LTE specification does not support 1Rx. In addition to 4G, supporting 5G in smart watches will be even more challenging for RF design
      To support 1Rx UE in specification will ensure the UE performance and consistency and provide a possibility for network/operator to identify the RedCap device (1Rx or 2Rx) according to the capability reporting.
  For smart wearables, the compact device form factor will result in high Rx antenna correlations in the case of multiple Rx antennas at the UE sides, thus large throughput degradation is expected compared to the ideal antenna assumption (low correlation ensured by sufficient antenna separation)
  Based on initial evaluation results:
      Considering practical wearable implementations, 2Rx with high antenna correlations has dramatic throughput loss compared to typical antenna separation possible for cell phones (e.g. 0.8lamda).
      For typical operation with SIR=5/10/15dB, at the range of mid to high SNR, the gain by 2Rx with high antenna correlations is marginal (less than 10%) compared to 1Rx.
Observations

## Slide 3
Evaluation results
Parameter | Value
Carrier frequency for evaluation | 3 GHz
Channel model | CDL-D , delay spread: 30ns
UE speed | 3 km/h
BS antenna configuration | 2 Tx antenna ports configured with ±45° polarization in CDL-D
UE antenna configuration | 2 Rx antenna ports configured with dual 90° polarization in CDL-D
PDSCH | 8PRB ,12 symbols， SCS=15kHz
Transmission scheme | TypeI codebook with PRG4
CSI-RS | 24PRB with 80ms period
Receiver assumption | Realistic channel estimation and adaptive MMSE-IRC equalizer
Adaptation function | AMC enabled, RI adaptation enabled, HARQ enabled