## Slide 1
3GPP TSG RAN Meeting #91e RP-210322
Electronic Meeting, Mar. 22-26, 2021
Source: vivo
Document for: Discussion & Decision
Agenda Item: 9.13
Support of almost-zero-power (AZP) wake-up signals and PA-less device operation in Rel-18

## Slide 2
  IDLE model activities contributes power powers for Smartphone, wearables , IoT
    Almost 50% of the power consumption is contributed by IDLE mode activities, including deep sleep, paging monitoring, and cell search/measurements
Idle mode power saving is critical for UE battery life, e.g. RedCap TR38.875
    For industrial sensors, the battery should last at least few years
    For wearables, the battery of the device should last 1-2 weeks
Almost-Zero Power (AZP) wake-up receiver
Background
50%
Figure 1. Components of IDLE state power consumption [1]
R1-1813446, UE Power Saving Evaluation Methodology,Qualcomm Incorporated, 3GPP RAN1#95
Observation:
Reducing IDLE power consumption for some type of UE, some traffic type is useful.
However, UE needs to keep alert even when keep asleep, i.e., periodically wake-up

## Slide 3
  ‘Periodic based’: Currently, UE periodically inquiry wake-up or not (e.g., paging)
  ‘Event-driven based’: NW sends wake-up command to UE without requiring UE to stay at ‘asleep-yet-alert’ state
Almost-Zero Power (AZP) wake-up receiver
Reconsider the design by minimizing asleep-yet-alert operation
Following legacy 3GPP design philosophy, UE keeps asleep-yet-alert state,
Power in sleep mode dominates if wakeup events are sufficiently infrequent
UE almost zero power standby for wake-up signal, i.e., almost zero-consumption ‘alert’ operation
Reconsider the design by minimizing asleep-yet-alert operation
Passive WUS receiver
  Passive envelope detector (ED) that minimizes the input noise-equivalent power (NEP) of the RF front-end, e.g., CMOS RF front-end is co-designed with a discrete tapped capacitor transformer to maximize the signal-to-noise ratio at the output of the ED [1]
[1] http://bioee.ucsd.edu/papers/A%20Near-Zero-Power%20Wake-Up%20Receiver%20Achieving%20-69-dBm%20Sensitivity%20-%20Hall%20(JSSC,%202018).pdf
Figure 2. Block diagram of the wakeup receiver showing waveforms from RF input through digital wakeup output.
To save power, traditional periodic based wake-up approach use extended DRX (e-DRX). However, it is only practice for delay insensitive device (e.g., IoT), it is not suitable for watch/glass…

## Slide 4
    Traditionally UE power consumption, RF + baseband @ RRC IDLE
      Power consumption about~20mW, and RF sensitivity ~-100dBm [1]
      Note: extend DRX can reduce IDLE power, with
    Passive circuit: passive envelope detector
      Power consumption 7.4nW, and RF sensitivity -71dBm @433MHz [2]
      Power consumption 99W, and RF sensitivity -97dBm @2.4GHz [3]
      Power consumption 45W, and RF sensitivity -87dBm @900MHz [4]
      IEEE 802.11ba, Wake-Up Receiver (WUR) Study Group
        Target Power 100𝝁W. Target transmission range: LP-WUR = Today’s 802.11 [5]
Almost-Zero Power (AZP) wake-up receiver
Comparing with state-of-art approaches (1)
Based on TD-LTE terminal
A -76dBm 7.4nW Wakeup Radio with Automatic Offset Compensation, Jesse Moody et al.
A −97dBm-sensitivity interferer-resilient 2.4GHz wake-up receiver using dual-IF multi-N-Path architecture in 65nm CMOS, Camilo Salazar et al
Abe, VLSI’14
Proposal for Wake-Up Receiver (WUR) Study Group, IEEE 802.11-16/0722r1
Observation: 100x~1000x power reduction is feasible by passive circuit as WUS receiver, with some sensitivity degradation
CMOS RF front-end which is designed for low power receiver with enough receiving sensitivity is being popularly studied
Figure 3. Year of Use estimation, standby only

## Slide 5
Almost-Zero Power (AZP) wake-up receiver
Comparing with state-of-art approaches (2)
A -76dBm 7.4nW Wakeup Radio with Automatic Offset Compensation, Jesse Moody, et.al, ISSCC 2018

## Slide 6
Almost-Zero Power (AZP) wake-up receiver
Design consideration
Overall system consists of communication radio (LTE/NR/NB-IoT…) + AZP Wake-up receiver (WUR)
  The AZP receiver is not intended for data transmission/ reception, it is intended for “wake-up” purposes only;
    It is ALWAYS active when the communication radio is off.
    Design performance metrics
        With probability of missed detection and false wakeup rate <1/hr
        Wakeup sensitivity, e.g., [-70] dBm, - compute the energy required for the wakeup signal detection
        coverage area based on a given Tx power and receiver sensitivity
        [50 ~ 100uW] standby power consumption
  The main communication Radio is intended for data transmission and reception
    AZP receiver wakes up the communication radio when there is data for receiving.
  The AZP receiver is regarded as supplementary module to the main communication radio module. Functions for AZP wake-up receiver is,
    Wake-up, simple digital baseband processing (e.g., sequence decoding), possible simple packet decoding and etc.
Design should consider the impact to network/UE performance
    Network controls UE behavior
Turn OFF AZP WUR
“traditional IDLE mode”
Turn ON AZP WUR
“Low-power-consumption standby”
Comm.
AZP-WUR
50 ~ 100 uW
Comm.
AZP-WUR
50 ~ 100 uW
Wake-up
Figure 4. AZP WUR is supplementary module to the main communication radio module
Figure 5. network controlled turn on/off AZP receiver

## Slide 7
PA-less operation
PAE and P_DC
Figure 1. Power efficiency (marked red when less than 5%), N78 and N41
Two PA implementation choices: 1) Constant 4.2V P_DC; 2) APT (adaptive power tracking)
    To support a new UE power class, e.g., up to [10~15] dBm for PA less operation
      Uu UL
      Sidelink
    Cost perspective:
      About 10% Relative cost saving for a reduction of transmit power (3GPP TR36.888)
    Power perspective:
      The PAE (PA efficiency) is very low (less than 5%) when Tx power is 0-10 dBm
      The bottom power of PA is still large even with APT. PA less operation can further eliminate this part of power consumption, e.g., 180mW for N78 (which is 20x idle standby power consumption)

## Slide 8
Preliminary feasibility evaluation
Observation: AZP WUS are feasible for 85%~95% UEs when the receiver sensitivity is -70dBm, and 100% UE when the receiver sensitivity is -90dBm
Observation: 10dBm Tx power class is sufficient for 100% UEs in InH scenario, and for 80% UEs with 20MHz Tx BW , or for 95% UEs with 5MHz Tx BW

## Slide 9
Almost zero power wake-up receiver
Justification
    Reducing IDLE power consumption for some type of UE, some traffic type is useful. However, in current design, UE needs to keep alert even when it is asleep, i.e., periodically wake-up
    Academic and IEEE design proves 100x~1000x power reduction is feasible by passive circuit as WUS receiver, with some sensitivity degradation
Proposals
    To study and support the AZP WUS enabled by passive receiver for stand-by UE power saving in Rel-18
PA-less operation
Justification
    For low Tx power transmission (0 ~ 10 dBm) for UE, The PAE (PA efficiency) is very low (less than 5%) .
    10dBm Tx power class is sufficient for 100% UEs in InH scenario, and for 80% UEs with 20MHz Tx BW , or for 95% UEs with 5MHz Tx BW
Proposals
    To study and support the lower Tx power class and PA-less device operation in Rel-18
  Summary
Proposals for Rel-18