## Slide 1
Plan for RAN Slicing SI and WI
CMCC
3GPP TSG RAN Meeting #91e RP-210398
Electronic Meeting, March 16-26, 2021

## Slide 2
Status for RAN slicing SI
RAN2 conclusion:
  From RAN2 viewpoint, the RAN slicing SI can be concluded
RAN3 agreements on the SI status:
  RAN3 proposes to extend the SI with one quarter in RAN3 and do down-selection during the extended SI.
  Common understanding is that, extending the RAN3 part of this SI would not impact the start of potential normative work in RAN2

## Slide 3
Schedule Plan for the RAN slicing SI and WI
Proposal:
  RAN2 starts RAN Slicing WI in 2021Q2
  RAN3 extend the SI with one quarter
  Update the scope of WID in 2021.6 to capture objectives of RAN3.
SI
RAN3 extended
WI
2021.3
2021.6
2022.3

## Slide 4
Objective
The work item aims to standardize the enhancement on RAN support of network slicing. Detailed objectives of the work item are:
Support slice based cell selection and reselection, specify mechanisms and signalling including [RAN2]
  To assist cell reselection, broadcast the supported slice info of the current cell and neighbour cells, and cell reselection priority per slice in system information message.
  To assist cell reselection, include the slice info (with similar information as slice info in SI message) in RRCRelease message
  To assist cell selection, if needed, broadcast supported slice of serving cell in SI message if SIB1 concerns can be addressed
Support slice based RACH configuration, specify mechanisms and signalling including [RAN2]
  Configure separated PRACH configuration (e.g., transmission occasions of time-frequency domain and preambles) for slice or slice group
  Configure RACH parameters prioritization (e.g., scalingFactorBI and powerRampingStepHighPriority) for slice or slice group
Note: The use of RAN slicing in given cells shall not prevent from accessibility for Rel-15 and Rel-16 UEs.
Note: RAN3 objectives to be added after down-selection of solutions finish.
Note: This work item should take SA2 output on slicing enhancement into consideration if RAN impacts are identified.