## Slide 1: Motivation for new SI: Study on Duplexing Flexibility for NR
3GPP TSG RAN Meeting #91-e
Electronic Meeting, March 16 - 26, 2021
RP-210453
Agenda Item: 15

## Slide 2
Motivation
Justification
  New service types (e.g., XR service, AI based service), New device type (e.g., Self-driving Car)
    Data traffic for both DL and UL direction can be heavy and dynamically appeared. It is required that data packet delivery is finished within a short time duration.
  Using unpaired spectrum
    Static TDD configuration and half duplex has a limitation of UL maximum throughput and latency problem.
    Dynamic TDD configuration has an potential problem which is inter-operator interference issue.
  Full duplex in unpaired spectrum provides enhancement of DL/UL resource utilization and reduction of DL/UL transmission latency by relaxing restriction of exclusive DL-UL resource utilization
Objective
  Study support of intra-carrier subband-wise and spectrum-sharing Full Duplex
    “gNB FD1) & UE HD2)” and “gNB FD & UE FD”
    Frequency range 1 (Unpaired Spectrum), Frequency range 2 and potentially Beyond 52.6GHz
UL
DL
Carrier #0
Frequency
Carrier #0
Frequency
DL
UL
Subband-wise Full Duplex
Spectrum-sharing Full Duplex
1) FD: Full Duplex, 2) HD: Half Duplex

## Slide 3
Performance Evaluation (SLS)
Target scenarios for performance comparison
Initial Evaluation Result
  Average UE packet delay (DL)
    Observation: Average UE Packet Delay is reduced and 50% UE throughput is enhanced, when Full duplex is applied.
Average UE packet delay (UL)
HD only | 103.91
HD and SB-FD | 132.02
SB-FD only | 144.04
50% UE DL Throughput (Mbps)
HD only | 21.55
HD and SB-FD | 31.93
SB-FD only | 35.56
50% UE UL Throughput (Mbps)

## Slide 4
Potential Scopes
Feasibility study of Full Duplex operation in gNB – UE [RAN1, RAN4]
  Define/prioritize scenarios for Full Duplex operation in terms of some aspects such as:
    Frequency resource utilization (e.g., separated frequency resource in a carrier is used for DL and UL, same frequency resource in a carrier is used for simultaneous operation of both DL and UL), etc.
    Frequency range (e.g., FR1, FR2)
    Deployment scenario (e.g., Rural, Urban, Indoor, Isolated)
    Antenna configuration (e.g., Single-/multi-panel, Co-located/distributed antenna),
  Note1: In a resource allocation perspective, Full Duplex operation includes simultaneous TX-RX in a same carrier
  Note2: The study may focus on unpaired spectrum, but necessity of enhancements for other scenarios(e.g. paired spectrum, sidelink) may be considered further
Study standardization impacts for the selected scenarios for Full Duplex operation [RAN1]
  Resource allocation (e.g., BWP)
  Interference handling (i.e., self-interference, UE-UE interference, gNB-gNB interference)
  MIMO operation (e.g., Beam management, Reference signal, CSI measurement, Multi-TRP/Cell)
  Duplex adaptation

## Slide 5
Annex 1. Evaluation Assumption for SLS
Deployment Scenario
  Carrier frequency:
    2GHz (Macro Layer), 3.5GHz (Micro Layer)
  Layout: Two layers
    Macro layer: Hex. Grid, 19 BSs
    Micro layer: Random drop, 3 micro cells per macro sector
    Min. distance btw macro-to-macro: 500m
    Min. distance btw macro-to-micro: 40m
    Min. distance btw micro-to-micro: 40m
  UE distribution
    855 micro UEs (5 UEs per micro cell in average)
    80% of indoor UEs, 20% of outdoor UEs
    Min. distance btw macro-to-UE: 35m
    Min. distance btw micro-to-UE: 10m
  Tx power: 33dBm (Micro), 23dBm (UE)
  Antenna configuration
    BS: (M, N, P, Mg, Ng) = (8, 8, 2, 1, 1), (dH, dV) = (0.5, 0.8)λ
    UE: (M, N, P, Mg, Ng) = (1, 1, 2, 1, 1)
Interference
  ACIR for CLI:
    43 dB(ACIR BS-BS), 28 dB (ACIR UE-UE)
  Self Interference Cancellation: 80dB
Traffic model
  FTP traffic model 3
    Downlink: 10 packets/sec/UE, 20KB/packet
    Uplink: 10 packets/sec/UE, 5KB/packet
System Parameters
  System BW/SCS: 50MHz / 15kHz (270RBs)
  DL/UL resource pattern
    Half Duplex only: DDDUU
    Half Duplex + SB_Full Duplex: DSSSU
    (S:DL and UL PRB ratio in S slot = 2:1, No Guard band)
    SB_Full Duplex only: SSSSS
    (S:DL and UL PRB ratio in S slot = 3:2, No Guard band)
  Resource pattern flexibility
    Static and common DL/UL resource pattern among cells
  HARQ
    Min. HARQ retransmission delay: 8 slots
    Target BLER for initial transmission: 0.1
  Rank-1
Performance Metric
  UE average DL/UL traffic delay (slot)
    Traffic delay: Slot index (Packet transmission completion) - Slot index (Packet is generated)
    Minimum traffic delay: 1 slot
  UE average DL/UL throughput (Mbps)
    Average throughput = sum ( Packet size/traffic delay(n) ) / N

## Slide 6
Annex 2. Intra-cell UE2UE Cross Link Interference
Measurement Environment
  Deployment
  Indoor (Parking lot)
  One gNB (Wideband Full Duplex operation for simult. DL &UL)
  BW: 100MHz, Center Frequency: 3.5GHz
  1Tx-1Rx, Tx power (5dBm)
  One aggressor UE (UL) :
  2Tx, Tx power (5, -5, -15, -25dBm, & No Tx)
  6 candidate locations
  One victim UE (DL):
  2Rx
  4 candidate locations
Observation
  Measured SINR (dB) of victim UE is varying depending on Tx power of aggressor UE, and distance between aggressor UE and victim UE.
  In many cases (e.g., lower Tx power for aggressor UE, or longer distance between victim UE and aggressor UE), intra-cell UE2UE CLI is negligible.
  It seems that the intra-cell UE2UE CLI is manageable by cross-Link Interference (CLI) mitigation schemes and network scheduling.
<Deployment for CLI measurement of Victim UE>
Candidate Locations of Aggressor UE for transmission
A1 (3m,10m) A7(20m,10m)
A3 (3m,30m) A9(20m,30m)
A6 (3m,60m) A12(20m,60m)
Candidate Locations of Victim UE for reception
V1 (0m,10m)
V2 (0m,20m)
V4 (0m,40m)
V6 (0m,60m)

## Slide 7
Annex 2. Intra-cell UE2UE Cross Link Interference
UE2UE CLI Measurement Result
  Victim UE1
  Victim UE4
  Victim UE2
  Victim UE6
Source of severe UE2UE CLI to victim UE

## Slide 8
Annex 3. UE2UE Adjacent Carrier Interference
Observation
  ACI from a far UE is negligible.
  ACI from a near UE affects to received signal quality of victim UE. Power of ACI is diminished when frequency position for UL signal transmission of aggressor UE is far from the frequency position for DL signal reception of victim UE.
  It seems that the UE2UE ACI is manageable by network scheduling.
<Deployment for ACI measurement of Victim UE>
Candidate Locations of Aggressor UE for transmission
<Adjacent Carrier Interference>
Aggressor UE #2
(3m,60m)
Candidate Locations of Victim UE for reception
Victim UE#2
(0m,60m)
15dB
2.5dB
5 dB
Measurement Environment
  One aggressor UE (UL Tx) : Center Frequency 3.75GHz
  One gNB (DL Tx): Center Frequency 3.85GHz
  One victim UE (DL Rx): Subband (20MHz) wise DL reception
Measurement Result
Aggressor UE #1
(3m,10m)