## Slide 1: Considerations on Context Fetch scenarios for NR SDT
Ericsson
3GPP TSG RAN#91
Electronic Meeting
March 16th -26th 2021
Agenda Item: 9.7.11
RP-210509

## Slide 2: Current status
SDT WID objectives include the following:
  Context fetch and data forwarding (with and without anchor relocation) in INACTIVE state for RACH-based solutions [RAN2, RAN3]
RAN2 and RAN3 had some initial discussion on how to support UE context retrieval, however there is no analysis on the scenarios, especially for "without anchor relocation" case.
In the legacy, Context fetch without anchor relocation is possible during periodic RNA update when UE is in the RRC_INACTIVE state. The anchor gNB may decide not to relocate the UE context, thus failing the UE context retrieval procedure. Such case so far is not discussed for SDT, or it can be considered as corner case.

## Slide 3: Solutions and Proposal
Proposed network solutions:
  Support of SDT anchor relocation
    reuse the existing procedures with potential minor enhancements.
  Support of SDT without anchor relocation
    Option 1: retrieve all the UE context from the anchor gNB.
      Cons: similar as anchor relocation case with extra efforts, e.g., setting up new Xn tunnels.
    Option 2: fetch RLC config from UE context stored in the anchor gNB.
      Cons: jeopardize the failure procedure or introduce new procedure.
    Option 3: forward data from the receiving gNB to the anchor gNB directly without retrieval of any UE context.
      Cons: transport all the RLC PDUs over Xn.
Example procedure for without anchor relocation
Any of the solutions to support SDT without anchor relocation case will bring more latency by signaling exchange between network nodes and cause unnecessary complexity to the network. Based on the above, we don’t see the need to work on complicated solution for such a limited rare scenario without clear benefits.
Proposal: Remove the support of SDT without anchor relocation for Context Fetch and data forwarding.