## Slide 1
Introduction of BDS B2a and B3I
in A-GNSS in Rel-17
CAICT, CATT, CMCC, China Telecom, China Unicom, CBN, Huawei, HiSilicon, ZTE, MediaTek Inc., Spirent, vivo, Spreadtrum, OPPO, Xiaomi, Swift Navigation, Intel Corporation, Qualcomm Incorporated
RP-210565
3GPP TSG RAN Meeting #91-e
Electronic Meeting, March 16 - 26, 2021

## Slide 2
B1I signal(V3.0) and B1C signal(V1.0)of BeiDou Navigation Satellite System (BDS) have been supported in 3GPP in Rel-16.
“BeiDou Navigation Satellite System Signal In Space Interface Control Document Open Service Signal B2a (Version 1.0)” has been published by China Satellite Navigation Office, in December, 2017.
BeiDou Navigation Satellite System
Signal In Space Interface Control Document
Open Service Signal B3I (Version 1.0) has been
published by China Satellite Navigation Office,
in February 2018.
Introduction
Reference : China Satellite Navigation Office, http://www.beidou.gov.cn/xt/gfxz/201712/P020171226742357364174.pdf
http://www.beidou.gov.cn/xt/gfxz/201802/P020180209623601401189.pdf

## Slide 3
The main reasons that B2a signal and B3I signal will be supported in A-GNSS in Rel-17 are:
B2a signal and B3I signal offer the open global navigation service on B2 and B3 frequency. The third generation of BDS, i.e. “BDS-3”provides global navigation services;
A-GNSS dual frequency compatible interoperation receiver will include A-BDS;
Higher accuracy of A-BDS with dual/multi frequencies on B1, B2 or B3.
Higher processing efficiency with triple frequencies on B1, B2 and B3, by reducing the initial time for ambiguity fixed.
Motivation

## Slide 4
B1C, B2a and B3I signal
Signal Type | Constellation | Carrier Frequency | Modulation Mode | Received Power Level
B1C | MEO/IGSO satellite | 1575.42MHz | BOC | MEO: -159dBW IGSO: -161dBW （with 0 dBi RHCP receiving antenna ）
B2a | IGSO/MEO | 1176.45MHZ | BPSK | MEO: -156dbW IGSO: -158dbW （with 0 dBi RHCP receiving antenna ）
B3I | GEO | 1268.520MHz | BPSK | -163dBW （with 0 dBi RHCP receiving antenna ）

## Slide 5
Discussion
Introduction of new BDS signal has been captured in the NR ePOS WID (RP-193099) in RP#86 meeting. But it was removed in SID when the WID was changed into SID because there is no need to study it.
So the current NR ePOS WID should include it in Rel-17.
B2a and B3I signals are expected to support in both 4G and 5G network as early as possible by the A-BDS global navigation ecosystem so more devices over the world will support A-BDS with high accuracy.
Proposal 1: Both B2a and B3I signals should be introduced in A-GNSS in 4G and 5G in Rel-17.

## Slide 6
Discussion
Since the requirement from A-BDS ecosystem is to introduce both BDS signals in both 4G and 5G but the NR ePOS WID is mainly for NR, so how to handle it can be discussed. There are two alternatives:
Alt 1: include B2a and B3I signals in current NR positioning WID with a note to clarify they should be supported in 4G also.
Alt 2: include B2a and B3I signals in current NR positioning WID for 5G only. And B2a and B3I signals for 4G will be supported in LTE TEI17 or a new LTE WI (note: only stage 2 CR is impacted for core part).
Proposal 2: RAN is kindly requested to discuss and decide how to support BDS signals in both 4G and 5G in Rel-17.

## Slide 7
Proposals
Proposal 1: Both B2a and B3I signals should be introduced in A-GNSS in 4G and 5G in Rel-17.
Proposal 2: RAN is kindly requested to discuss and decide how to support BDS signals in both 4G and 5G in Rel-17.
  Alt 1: include B2a and B3I signals in current NR positioning WID with a note to clarify they should be supported in 4G also.
  Alt 2: include B2a and B3I signals in current NR positioning WID for 5G only. And B2a and B3I signals for 4G will be supported in LTE TEI17 or a new LTE WI (note: only stage 2 CR is impacted for core part).

## Slide 8
THANK YOU