## Slide 1: Background to corrections of Pcmax for UL CA with uplink Tx switching capability
Ericsson
3GPP TSG-RAN Meeting #91-e
Electronic meeting, 16 – 26 March 2021
RP-210572

## Slide 2: Background: why a RAN matter?
For an UL CA configuration with UL TX switching (switching between carrier 1 and carrier 2), RAN#88-e approved a Rel-16 CR [1] enabling 3 dB power boosting on carrier2 allowing UL CA PC3 implementations with the same power capability as the SUL/NUL alternative; 26 dBm on carrier2
  Same methods for facilitating SAR compliance (unspecified in Rel-16, up to UE implementation)
The RAN#88-e agreement for switched UL captured in the WF in [2]. The WF allows maintenance:
  “No other RAN4 spec impact due to change introduced related to this power boosting and UL Tx switching between case 1 and case 2
    No other RAN4 spec impact due to the change introduced related to this power boosting and UL Tx switching between case 1 and case 2 does not preclude companies’ maintenance Cat F CR, which can be agreed based on consensus.”
Since RAN4#96 (August 2020) Ericsson has provided RAN4 Cat-F CRs with correction of the total configured maximum power PCMAX for CA that does not allow 3 dB boosting, limited to 23 dBm for PC3
  Reason for change: the UE would apply prioritization of the transmissions according to clause 7.5 of 38.213 already at PCMAX = 23 dBm for UL CA PC3, 26 dBm on carrier2 is obviously impossible
One company consistently claiming that the RAN4 specification is not broken or that new functionality is included, and that changes are not needed
The RAN#88-e agreement for UL CA can not be implemented without violating the current version of the specification, RAN4 unable to agree on necessary changes for Rel-16
RAN to reconfirm that maintenance is allowed and approve necessary changes (already seen by RAN4)

## Slide 3: Background to changes
For an inter-band UL CA configuration with UL TX switching (switching between carrier 1 and carrier 2), the RAN#88-e approved CR should enable 3 dB power boosting on carrier2 allowing UL CA PC3 implementations with the same power capability as the SUL/NUL alternative; 26 dBm on carrier2
  in [1] the power boosting was implemented in the specification of the time masks for UL CA, but not in the specification of the configured maximum output power for UL CA, the PCMAX
The maximum power on carrier 2 is boosted by 3 dB if the uplinkTxSwitchingPowerBoosting-r16 is enabled and the capability uplinkTxSwitching-PowerBoosting-r16 is supported by the UE – only then
Reason for change: the PCMAX for UL CA in 38.101-1 does not allow 3 dB power boosting for the BC for UL CA PC3. The UE would apply power prioritization of the transmissions according to clause 7.5 of 38.213 already at PCMAX = 23 dBm, 26 dBm on carrier2 is obviously impossible
  carrier2 can only attain 23 dBm according to 38.213, UE power reductions occur when PCMAX (as specified by RAN4) is exceeded
from 38.331, defined for PC3 only

## Slide 4: The necessary changes in the (company) CR
When 38.331 conditions met for boosting (only then), increase the PCMAX by 3 dB for UL CA PC3
Allow the UE to use PC2 MPR on carrier2 in that case
Consequences if not approved: carrier2 boosting is impossible (cap at 23 dBm total power)
The changes in the company CR [3] identical to those in [4] discussed by RAN4
Green highlight the same as for standard UL CA

## Slide 5: UL CA and SUL options for TX switching on the same footing for Rel-16
Comparing to the SUL/NUL option of TX switching without approval of [3], a corresponding restriction would be a cap of the total NUL/SUL power of 23 dBm, which would obviously also preclude carrier2 transmissions at 26 dBm for SUL/NUL
  the power prioritization in 38.213 also applies to NUL/SUL carriers
However, the SUL output power specification does not contain any limits on the total power, but the issues w r t SAR for SUL/NUL and UL CA with boosting are the same
  same methods for facilitating SAR in the UL (up to UE implementation)

## Slide 6: Proposal
The company Cat-F CR in [3] approved for Rel-16 (maintenance)
  the CR has been seen by RAN4
UE implementations should not have to violate RAN1/RAN4/RAN5 specifications to support the RAN#88-e agreement for UL CA PC3 with TX switching

## Slide 7: References
RP-201338, ”CR to TS 38.101-1: Switching time mask between two uplink carriers in UL CA and SUL”, China Telecom, CMCC, China Unicom, KDDI, Spreadtrum, CATT, CHTTL, MediaTek, OPPO, Huawei, HiSilicon, vivo, Xiaomi, Orange, Apple, Nokia, Nokia Shanghai Bell, ZTE, Ericsson, Qualcomm
RP-201365, ”Final Proposal of Switched_UL”, Nokia (moderator)
RP-210573, ”Modification of Pcmax for UL CA with uplink Tx switching capability”, Ericsson
R4-2103159, ”Modification of Pcmax for UL CA with uplink Tx switching capability”, Ericsson