## Slide 1: Agenda Item : 9.13 Source : InterDigital Communications Title : On the Scope of Rel-18 PHY Layer Enhancements using AI-based Solutions Document for : Discussion and Decision
3GPP TSG RAN Meeting #91e RP-210672
Electronic Meeting, March 18th – 24th, 2021

## Slide 2: Possible PHY Layer Enhancements for NR
MIMO CSI feedback
  CSI feedback compression
  CSI prediction
RS overhead reduction
  Adaptive RS density based on UE AI processing capability
Mobility/Beam management optimizations
  Optimized beam measurements
  Predictive beam/mobility management
  Enhanced beam failure recovery
Positioning enhancements
  Improved accuracy in NLOS
  Robustness in presence of synchronization errors
AIML can be a useful tool to address a specific problem/optimization.

## Slide 3: Categorizing possible impact of AI solutions
OEM AI black box
  Placement of AI model: Local to the UE or gNB
  Training strategy: Implementation
  Benefits: Optimization of local processing targetting implementation based PHY performance improvement
  Possible Impacts: Details of AI model and training is out of scope of 3GPP, possibly new feedback from the UE
UE-based AI black box
  Placement of AI model: Local to the UE
  Training strategy: Offline, Online refinement possible
  Benefits: Optimization of system performance
  Possible Impacts: Details of AI model and training is out of scope of 3GPP, definition/indication of UE capability relating to AI processing, supported signaling for network control, feedback and procedures etc
Joint AI
  Placement of AI model: AI model at the UE and AI model at the gNB
  Training strategy: Offline, Online or Remote
  Benefits: Optimization of performance impacting multiple endpoints
  Possible Impacts: Signaling to enable configuration of AI model, support for model training and/or download, definition/indication of UE capability relating to AI processing, potential new feedback, supported signaling for network control, feedback and procedures etc
Impacts to specification and complexity depend on placement and training method for the AI solution

## Slide 4: Possible challenges
Challenge 1: Data sets for AI model training
  Do we have agree on data sets to use for evaluation ?
  What are the assumptions to generate and/or collect data ?
  How to ensure training data to represents realistic environment both in terms of quality and quantity ?
  Would synthetic data be sufficient for evaluation ? Should the synthetic data be augmented with real data?
Challenge 2: Definition of UE capability w.r.t AI processing
  How to define UE capability in terms of memory, processing power, latency, support for various AI model architectures etc
Challenge 3: Interoperable AI model representation
  Applicable for remote training and AI model download scenarios
Challenge 4: What is the methodology used to evaluate AI-based solutions?
  What methodology should RAN use to test conformance and performance ?
  What methodology should RAN use specifying support for AI-based solutions ?
Challenge 5: Predictable and guaranteed performance of AI
  How to ensure predictable performance from a AI model ?
  Scope of the work should limit the challenges that needs to be addressed within Rel-18 time frame

## Slide 5: Proposal for Rel-18 SID Scope
Study on evaluation of AI-based PHY enhancements
  Identify use case and deployment scenarios.
  Study performance evaluation methodology for AI based solutions.
    Study assumptions on the AI models, algorithms, training aspects and data sets.
  Study standardization impacts for selected use cases for which AI methods are shown to be beneficial.
  Study characterization and signaling of UE capabilities w.r.t AI processing
  For a first RAN-led SI with AI-based enhancements, we propose to focus on use cases, deployments and evaluation methodology

## Slide 6: Thank you