## Slide 1: Analysis of RAN work for Layer-2 Sidelink Relay
Apple, Futurewei, InterDigital, Huawei, HiSilicon, MediaTek Inc., Convida Wireless
RP-210687
3GPP TSG RAN Meeting #91e
Electronic Meeting, March 16-26, 2021

## Slide 2: Introduction
Major conclusions of the RAN2 study
  Mechanisms for L2 relay and L3 relay have been studied and identified by RAN2, striving for minimum specification impact.
  The standards impact of L2 relay is principally in RAN and the standards impact of L3 relay is principally in SA.
We analyze whether it is feasible to complete both Layer 2 UE-to-NW relay and Layer 2 UE-to-UE relay in the remaining timeframe of Rel-17
  Outline of the technical items and relative work amount.
  Comparison of RAN2 workload between Rel-17 SL relay vs. Rel-16 NR V2X

## Slide 3: Layer-2 relay work needed in RAN
Common for U2U & U2N and common for L2 and L3
  Relay/remote UE authorisation [RAN3]
  relay selection and reselection [RAN2]
  Discovery operations for Sidelink relaying [RAN2]
U2N specific:
  Control plane procedures (connection management, SI, paging, etc) [RAN2]
  Uu/PC5 Adaptation layer. [RAN2]
  QoS [RAN2]
  Service continuity [RAN2/RAN3]
U2U specific:
  Control procedures (including connection management) [RAN2]
  Adaptation layer design and other user plane protocol aspects. [RAN2]
  End-to-end security of relayed connection [RAN2]

## Slide 4: Analysis of workload for L2 UE-to-NW relay
Relay discovery and (re)selection: Minimum:
  Reuse the LTE-Prose relay discovery and (re)selection baseline.
  WI can discuss additional U2N specific AS layer criteria.
  Address the OLPC impact for PC5 link quality evaluation.
Control plane : Medium
  SI has laid out the baseline solutions for connection establishment, paging and SI forwarding & retrieval.
  RRC_INACTIVE state support.
User plane protocol stack: Minimum
  Uu adaptation header: U2U-specific, not sharing common design with U2N relay. (U2N may not have PC5 Adaptation header).
  PC5 Adaption for U2N can be deprioritized by assuming 1:1 mapping
Handover & service continuity: Medium
  gNB-controlled path switching for intra-gNB direct-indirect handover.
  Collaborate with RAN3 for inter-gNB handover solution.
End-to-End QoS: Medium
  E2E QoS Split into per-hop QoS as baseline solution specified in SA2.
  Signaling & procedure support and necessary enhancements to ensure E2E QoS (e.g., admission/congestion control).
Given the amount of “medium” and “minimum” work, an estimate of ~6 TUs are expected for U2N part.

## Slide 5: Analysis of workload for L2 UE-to-UE relay
Relay discovery and (re)selection: Minimum
  Share a common baseline solution with U2N relay
  WI can discuss U2U specific AS layer criteria (e.g., considering 2nd-hop PC5 link quality and load status).
  OLPC impact for PC5 link quality evaluation is common for both U2N and U2U, No extra work need.
Control plane procedures : Minimum
  Integrate Discovery/Connection establishment, and other CP enhancements for better performance.
  QoS is based on SA2 baseline solutions. No extra AS layer work.
User plane protocol stack: Medium
  PC5 adaptation Layer: U2U-specific, U2N relay may not have PC5 Adaptation header.
  Routing/forwarding mechanism based on adaptation header information
Handover between direct and indirect: Minimum
  No need to support inter-relay mobility in R17.
  Based on PC5 measurements, no Uu solution to reuse.
  Service continuity is not supported for U2U relay.
End-to-End U2U Security: Minimum
  PC5-S procedures over the top of AS layer to configure PDCP layer. Main work is up to SA2.
Given the amount of “medium” and “minimum” work, an estimate of ~3 TUs are expected for U2U part.

## Slide 6: Timeline resemblance: NR V2X vs. NR SL Relay
RAN2 completed R16 NR V2X WI from Q2 2019 to Q1 2020, it used 4 quarters and 6 WG meetings.
Similarly , 4 quarters left ( Q2 2021 to Q1 2022) towards the stage-3 freeze of R17.
2019
2020
2021
2022
R16 NR V2X
RAN2# | 105 bis | 106 | 107 | 107bis | 108 | 109
TU used | 2 | 2 | 2 | 3 | 3 | 3
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
R17 NR SL Relay
RAN2# | 113 bis | 114 | 115 | 115bis | 116 | 117
TU estimate | 1.5 | 1 | 2 | 2 | 2 | 2

## Slide 7: RAN2 work comparison of NR V2X and NR SL Relay
R16 created a new SL interface for NR, but R17 just need specify add-on procedures on top of existing interface.
SL relay work task in RAN2 is considerably less than NR V2X, as shown in table below
 | NR V2X | NR SL Relay | R17 vs. R16
Control plane (RRC, etc.) | New V2X SIB, resource pool configurations SLRB configurations New PC5-RRC protocol Support of flow-based Sidelink QoS Cross-RAT configuration/scheduling Congestion control Cell (re)selection | AS support for Relay (re)selection direct-indirect path switching End-to-end QoS support via relay SI forwarding Paging via relay | Less
User Plane (e.g., MAC/RLC/PDCP) | MAC/RLC/PDCP/SDAP PDU formats Mode 1 resource (Type 1/2 CG & DG) Mode 2 resource allocation & sensing Groupcast & unicast HARQ feedback Distance-based groupcast Uu/SL prioritization, preemption, re-evaluation Sidelink RLF/RLM Sidelink RLC AM support PDCP Security for SL Unicast | Uu Adaptation layer and header PC5 Adaptation Layer and header | Much less
RAN1 dependency | More TUs are spent on RAN1 and delays were caused by unsolved RAN1 issues. | No. RAN2 can progress more efficiently without relying on inputs from RAN1. | 

## Slide 8: Conclusion
Summary of the analysis:
  RAN2 workload for Layer 2 relay is about 9 TUs, with an estimate of 6 TUs and 3 TUs for U2N relay and U2U relay respectively, assuming some overlapping work in relay discovery and relay (re)selection can be reused for both.
  Compare to Rel-16 NR Sidelink, R17 relay work has relatively less technical tasks and should be completed within 4 quarters.
Conclusion:
  RAN is able to finish both L2 U2N and L2 U2U relay in Rel-17.