## Slide 1: WF on guidelines for Rel-17 FR1 CA/DC band combinations approval handling
Apple Inc., Skyworks Solutions Inc.
3GPP TSG-RAN #91-e
Electronic Meeting, March 16th – 26th
RP-210639

## Slide 2: Background
UE band combination basket work items block approval process has been implemented since LTE and continued in NR.
The framework has successfully facilitated the TR TP review process and improved RAN4 work efficiency on developing the UE RF requirements for majority of band combinations.
Nonetheless, there are certain band combinations which may require additional technical justifications or requirements not covered by the standard basket TR TP format and may not be suitable for block approval process.
This contribution is intended to provide guidelines for FR1 band combinations approval handling.

## Slide 3: Guidelines for Combinations Not for Block Approval
Inter-band CA/DC with adjacent or overlapping frequency ranges
  Need a discussion paper to address the front-end implementation feasibility and usage scenarios.
  Example combination: CA_n20-n28 where DL ranges partially overlap
Inter-band CA/DC with two or more bands below 1 GHz
  Need a discussion paper to address the front-end implementation feasibility and usage scenarios. The aspect of antenna configuration including diversity path and its implication to form factor shall be considered.
  UL CA needs further discussions if the corresponding DC combination only supports SUO.
  Same combinations which have been specified in LTE can waive the discussion paper.
Intra-band UL CA with 2 CCs where A-MPR requirements have not been specified (in basket WID not for block approval) – requires A-MPR requirements/study
Intra-band CA with more than 2 non-contiguous DL CCs with > 200 MHz frequency span
  Need a discussion paper to address the implementation feasibility including DL MIMO support.

## Slide 4: Band Combinations Which Need a New Feature Defined
Intra-band contiguous EN-DC with new bandwidth class, such as classes AC and CB
Intra-band contiguous UL CA with 3 CCs
UL CA with three or more non-contiguous CCs including
  Inter-band UL CA with UL in three or more bands
  Intra-band non-contiguous UL CA with three or more discrete UL CCs
  Inter-band UL CA consisting of intra-band non-contiguous UL CA
Note: these combinations are not allowed to request in basket WI.

## Slide 5: Additional Aspects
Band combinations which can be directly introduced in draft CR – No TP for TR required
  Adding DL intra-band CA to an existing inter-band combination (but not for intra-band UL CA) where DL intra-band CA has been specified.
  Adding > 3 FR1 band combinations (up to the maximum band numbers supported in current basket WI) if the corresponding fallbacks are complete.
  Adding FR2 band or existing FR2 CA to an existing FR1 combination.
Regional spectrum restriction is allowed with a clarification note, but not operator specific spectrum allocation.
UL configuration allowing SUO or mandating SUO shall be clearly stated in TP.
TDD-TDD supporting simultaneous Rx/Tx or not shall be clearly stated in TP.
Inter-band UL CA including intra-band contiguous UL CA, such as UL CA_n3-n41C
  Triple beat issue needs to be addressed. (refer to WF R4-2103097)

## Slide 6: Way Forward
Guidelines for Rel-17 FR1 CA/DC combinations approval that RAN4 will develop should be captured in the TR created in the SI on band combination handling.
The list of guidelines presented in this WF can be used as baseline for further discussions and refining in coming RAN4 meetings.
Dedicated agenda in coming RAN4 meetings can be arranged by RAN4 Chairman for guidelines which require further discussions.