## Slide 1: Status of RAN4 work on LTE CRS interference handling for NR UE
China Telecom, Intel Corporation
3GPP TSG RAN Meeting #92e
Electronic Meeting, June 14 - 18, 2021
Agenda: 9.7.4.3
Document for: Information
RP-211136

## Slide 2: Introduction (1/2)
The revised WID on “Further enhancement on NR demodulation performance” was approved at RAN #91e [1] to add the following objective on LTE CRS interference handling for NR UE.
Evaluate techniques to cope with CRS interference in scenarios with overlapping spectrum for LTE and NR
    Candidate reference receiver to enable neighboring cell CRS-IM
    The performance benefit of neighboring cell LTE CRS-IM over the existing rate matching solutions specified in Rel-15 and Rel-16 shall be evaluated.
    Feasibility of the considered solution regarding NR PDSCH processing timeline need to be checked.
    Priority will be given to solutions not having RAN1 specification impact.
    Synchronous network scenario is prioritized. As second priority, RAN4 could evaluate the feasibility and usefulness of the asynchronous network scenario and specify if feasible and useful.
    15 kHz SCS for NR is prioritized. RAN4 should evaluate the feasibility and usefulness of 30 kHz SCS for scenarios with LTE and NR deployed in neighboring BSs/areas and specify if feasible and useful.
Note: The work can be started from May 2021 meeting.

## Slide 3: Introduction (2/2)
Additionally, in [2], the following RAN plenary guidance was provided for this work:
  Performance evaluation of DSS wrt interference is needed first – collect company input
  Ask RAN4 to perform this evaluation until RAN#93E (September), to be reviewed at RAN#92E (June)
  As per the above RAN plenary guidance, this contribution summarizes the progress of this work in RAN4:
  In May RAN4 #99e meeting, RAN4 agreed the evaluation scenarios and detailed assumptions for the study phase, with details in [3].
  The main task for August RAN4 #100e meeting is to collect simulation results from interested companies and discuss if there is any potential impact to other WGs.

## Slide 4: RAN4 agreement on general scenario
General scenario
  Scenarios for initial LLS evaluation before RAN #93e
    Scenario 1: LTE and NR DSS, with 15kHz SCS
    Scenario 2: NR and LTE deployed in neighboring BSs/areas, with 15kHz SCS
  30 kHz SCS for scenario 2 can be deprioritized before RAN #93e
  Focus on synchronous network before RAN #93e
Scenario 1
Scenario 2

## Slide 5: RAN4 agreement on CRS-RM and CRS-IM schemes for evaluation
  CRS-RM schemes for performance comparison with PDSCH CRS-IM
  Assumption on CRS-IM (interference mitigation) receivers
  Both CRS-IC and LLR weighting for the initial performance evaluation
  FFS for performance requirements definition.
  FFS NW assistant information existed or not, companies are encouraged to bring analysis with different options.
  Number of CRS cells to be mitigated: 1 or 2 cells, and it is up to UE implementation.
 | No interference cell CRS handling | CRS rate matching (CRS-RM) | 
 |  | CRS-RM for 1 interference cell | CRS-RM for 2 interference cells
Scenario 1 | Rel-15 CRS-RM for serving cell | Rel-16 CRS-RM for 1 interference cell | Rel-15 RB symbol level RM for 2 interference cells
Scenario 2 | No RM | Rel-15 CRS-RM for 1 interference cell | Rel-16 CRS-RM for 2 interference cells
NOTE: Companies are encouraged to bring analysis on the performance impact on LTE cell due to Rel-16 RM.

## Slide 6
  Discuss if there is any potential impact to other WGs.
  Collection of simulation results before RAN4 #100e
  Based on the detailed assumptions agreed in [3], simulation results will be collected and calibrated in RAN4 draft reflector from Aug 2nd to 5th. Interested companies are encouraged to provide simulation results before the meeting if possible.
  Template for simulation result collection is provided in [4].
Work plan towards RAN4 #100e

## Slide 7: References
  [1] RP-210920, Revised WID on Further enhancement on NR demodulation performance, China Telecom, RAN #91e, March 2021.
  [2] RP-210906, Way forward on new proposals, Nokia (RAN chair), RAN #91e, March 2021.
  [3] R4-2108662, WF on CRS interference handling in scenarios with overlapping spectrum for LTE and NR, China Telecom, RAN4 #99e, May 2021.
  [4] R4-2108663, Template for simulation result collection for CRS interference handling, China Telecom, RAN4 #99e, May 2021.

## Slide 8
Thanks!