## Slide 1: Improved MSD for CA and DC
Qualcomm Incorporated, T-Mobile USA, Verizon, AT&T, DISH Network, TELUS, Deutsche Telekom, CMCC, CHTTL, KT Corp, Vodafone, BT plc., Telecom Italia, Bell Mobility
RP-211305
3GPP TSG-RAN #92-e
June 14th ‒ 18th, 2021
Electronic Meeting

## Slide 2: Background
Maximum sensitivity degradation (MSD) is specified for CA and DC configurations where there is Rx interference caused by Tx (i.e., harmonics, intermodulation products, etc)
MSD is sometimes specified to be very large, i.e., more than 20 or 30 dB! This is a severe impact to DL performance and renders CA practically unusable for most UE’s in the cell.
On the other hand, it has been observed and confirmed that some real-world devices perform much better than the specification, in excess of 20 dB better than the specification [5],[6]
Operators have indicated the benefit of being able to distinguish devices with much improved lower MSD from those with the currently specified MSD [1]
Currently in RAN4, there is an impasse between operators and vendors in the past 4 meetings on progressing this topic
  “No consensus on this sub-topic, it seems we have repeated the same situation for companies’ standpoints with last meeting.” [Moderator status summary from RAN4 #98bis-e]

## Slide 3: Proposal
3GPP specifies minimum performance requirements balancing both UE implementation feasibility and performance needed to meet operator/ecosystem objectives and use cases.
The currently specified MSD enables flexibility in UE implementation, but does not fulfill the operator’s needs for CA and DC.
  MSD is derived based on conservative component performance assumptions
  CA/DC combinations with large specified MSD may never be deployed by the operator since the specification is so poor
  Scheduling restrictions will need to be imposed across all UE’s reducing the efficiency and utilization of the available spectrum
Proposal 1: RAN4 to introduce a new UE capability bit to allow a UE indicate support for improved MSD
Proposal 2: RAN4 will choose a (preferably low single digit) improved MSD value that a UE could declare support for a given combination with a new capability bit
  RAN4 could either define a single improved MSD value for all the types of MSD, or it could choose one level for harmonics, one level for harmonic mixing, one level for cross-band isolation and one value for Intermods.
Proposal 3: The new capability would be signalled per UL/DL band combination
These proposals have already been presented at RAN4 #99-e [1], but not agreed due to objection from vendors. We believe that the needs of the operators have not been fully addressed during the discussion in RAN4. We also note that the capability is optional so a UE is not required to support improved performance if its design does not enable it to do so.

## Slide 4: Further discussion points
How to determine the improved MSD value [RAN4]
The details of the signaling need to be decided [RAN2/RAN4?]
Should this be limited to new combinations being specified, i.e., PC2 CA, or should this also apply (optionally) to existing combinations even PC3? [RAN4?]
Under what work item and release should this be carried out? [RAN]

## Slide 5: References
[1] R4-2107808, “Way forward for MSD improvement,” T-Mobile USA
[2] R4-2016440, “Improving PC2 MSD for EN-DC and UL CA,” Qualcomm Incorporated
[3] R4-2016854, “WF on MSD assumptions improvement for UE PC2 combinations,” China Telecom, Qualcomm, Verizon
[4] R4-2102415, “MSD for PC2 EN-DC and UL CA,” Qualcomm Incorporated
[5] R4-2110791, “Discussion on UE capability for improved PC2 MSD for EN-DC and NR CA,” CHTTL
[6] R4-2111492, “MSD and real-world implications,” T-Mobile USA, Deutsche Telekom, Verizon, CHTTL, AT&T, Dish Network