## Slide 1: Motivation: Measurement Requirements for “NeedForGap”
Ericsson, Huawei, HiSilicon
3GPP TSG-RAN Meeting #92-e
Electronic meeting, 14 – 18 Jun 2021
Agenda item: 9.5
Document for: Discussion
RP-211348

## Slide 2: Background
In Rel-16, the NeedForGap measurements has been introduced for NR SA only in RAN2 specification. It was specified in TS 38.331 Rel-16 as shown below:
NeedForGapsInfoNR information element -- ASN1START -- TAG-NeedForGapsInfoNR-START NeedForGapsInfoNR-r16 ::= SEQUENCE { intraFreq-needForGap-r16 NeedForGapsIntraFreqlist-r16, interFreq-needForGap-r16 NeedForGapsBandlistNR-r16 } NeedForGapsIntraFreqlist-r16 ::= SEQUENCE (SIZE (1.. maxNrofServingCells)) OF NeedForGapsIntraFreq-r16 NeedForGapsBandlistNR-r16 ::= SEQUENCE (SIZE (1..maxBands)) OF NeedForGapsNR-r16 NeedForGapsIntraFreq-r16 ::= SEQUENCE { servCellId-r16 ServCellIndex, gapIndicationIntra-r16 ENUMERATED {gap, no-gap} } NeedForGapsNR-r16 ::= SEQUENCE { bandNR-r16 FreqBandIndicatorNR, gapIndication-r16 ENUMERATED {gap, no-gap} } -- TAG-NeedForGapsInfoNR-STOP -- ASN1STOP

## Slide 3: Motivation
In Rel-16, to improve the system performance, UE can dynamically report ‘no gap’ by NeedForGap signalling which means UE can perform measurements without MG configuration.
In Rel-17, NCSG discussion is ongoing which also has a relation with NeedForGap. For example, the UE’s behaviour is unclear when it reports both ‘no gap’ and ‘NCSG’ for the same band.

## Slide 4: WF on Requirements for “NeedForGap”
Work scope:
  Limited to SSB based measurements configured via measurement objects in NR-SA only
  Study whether the additional interruption is allowed when UE reporting ‘no gap’
    Further define the interruption length, occasion and ratio, if the interruption is allowed
  Study the related requirements, such as CSSF, measurement period, scheduling restriction etc.
  No impact to other WG is expected.
Release:
  Specify UE requirements in R16 under TEI16.
Timeline/TU:
  1 TU in total:
    0.5 TU per RAN4 meeting over 2 RAN4 meetings (see next slide).

## Slide 5: Proposed Timeline/TU
RAN4 #100e(0.5TU)
  Discuss on
    the definition of ‘no gap’
      the interruption length, occasion and ratio, if the interruption is allowed
    measurement requirements based on the definition
  Agreements on
    the definition of ‘no gap’
    the interruption length, occasion, if the interruption is allowed
RAN4 #101e(0.5TU)
  Discussion on
    remaining issues on interruption, if the interruption is allowed
    measurement requirements
  Agreements on
    Conclusion on the remaining RRM impact.
    CR on TS38.133.

## Slide 6: Annex: RAN4 WF approved at RAN4#99-e

## Slide 7: WF on NeedForGap measurements
Ericsson, Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #99-e
Electronic meeting, 19 – 27 May 2021
Agenda item: 5.1.7.3
Document for: Approval
R4-2108039
Session chair: There is no consensus to do the work in Rel-16 TEI due to potentially larger scope and late stage of Rel-16. The WF is agreeable to RAN4 and provides a set of candidate objectives. WF is noted as no work is planned. Further discussion in the plenary is recommended on whether and how to handle this.

## Slide 8: Background
In Rel-16 TEI, RAN2 has introduced NeedForGapsInfoNR capability for NR measurement as follow.
The related requirements for NeedForGap are not defined in Rel-16.
NeedForGapsInfoNR information element -- ASN1START -- TAG-NeedForGapsInfoNR-START NeedForGapsInfoNR-r16 ::= SEQUENCE { intraFreq-needForGap-r16 NeedForGapsIntraFreqlist-r16, interFreq-needForGap-r16 NeedForGapsBandlistNR-r16 } NeedForGapsIntraFreqlist-r16 ::= SEQUENCE (SIZE (1.. maxNrofServingCells)) OF NeedForGapsIntraFreq-r16 NeedForGapsBandlistNR-r16 ::= SEQUENCE (SIZE (1..maxBands)) OF NeedForGapsNR-r16 NeedForGapsIntraFreq-r16 ::= SEQUENCE { servCellId-r16 ServCellIndex, gapIndicationIntra-r16 ENUMERATED {gap, no-gap} } NeedForGapsNR-r16 ::= SEQUENCE { bandNR-r16 FreqBandIndicatorNR, gapIndication-r16 ENUMERATED {gap, no-gap} } -- TAG-NeedForGapsInfoNR-STOP -- ASN1STOP

## Slide 9: Agreements
‘NeedForGap’ in Rel-16 is only applied in NR SA.

## Slide 10: Work Scope
Potential new objective - NeedForGap for NR-SA only
  Limited to SSB based measurements configured via measurement objects
  Study whether the additional interruption is allowed when UE reporting ‘no gap’
    Further define the interruption length, occasion and ratio, if the interruption is allowed
  Study the related requirements, such as CSSF, measurement period, scheduling restriction etc.
  RAN4 to further consider the relation with other UE capabilities, such as NCSG etc.
  Analyse other WG impact although impact is not expected.
  Decide if it is feasible that the UE requirements are defined in R16 or release independent from Rel-16.