## Slide 1: On the need for RedCap UEs early identification based on the number of RX branches
Telecom Italia, Deutsche Telekom, BT
3GPP TSG RAN#92-e 14th – 18th June 2021 Online | TDoc RP-211360 Agenda Item 9.7.1.7 - Support for reduced capability NR devices [RAN1 WI: NR_redcap]

## Slide 2: Background (1/2)
For the Rel-17 RedCap WID [1] the objectives related to the reduced minimum number of RX branches were agreed in RAN#91-e (March 2021) as follows
While the objective related to the RedCap UE early indication during initial access was defined as follows

## Slide 3: Background (2/2)
In RAN1#104bis-e meeting (April 2021) whether the information on the number of Rx branches of a RedCap UE during initial access (i.e. RACH) was discussed and the following agreements were achieved [2]
RAN2 discussed the same topic during the RAN2#114-e meeting (May 2021) and agreed the following [3]

## Slide 4: Observations
Based on the background the functionality of early indication of RedCap UEs is in the WID scope, but the information related to the number of Rx branches is not included
The introduction of the RedCap UE early indication as an outcome of the Study Item was motivated by the need to accommodate RAN1 requirements listed in TR 38.875 §11.1.1 [4], in particular coverage recovery (including link adaptation) for RACH messages following Msg1
The main impact of a UE having 1 Rx branch instead of 2 Rx branches is worse coverage, so it would be better for the network to be aware of the number of Rx branches supported by the RedCap UE during initial access so to apply the most effective coverage compensation technique and avoid RACH failures
As per the current agreements in RAN2, not having the information on the number of Rx branches in the early indication during initial access might lead to the assumption at network side that any RedCap UE has 1 Rx branch until the full UE capabilities have been retrieved [5] which for the co-signing companies represents an inefficiency in the RACH procedure given the motivations above
From RAN2 perspective the only motivation to include the number of Rx branches in the RedCap UE early indication is to allow the network to reject the RedCap UE with 1 Rx based on the load and operators’ access control strategy
  However this could be possible via the SIB1 broadcasting cell barring information provided separately for UEs with 1Rx and Rx branches, so that a RedCap UE with 1Rx branch will not consume/contend for radio resources for initial access

## Slide 5: Proposals
Proposal 1: include the information on the number of Rx branches supported by a RedCap UE within the early indication during the initial access
Proposal 1b: if Proposal 1 is agreed, RAN to send a LS to RAN1 and RAN2 to take the agreement into account for their normative work
Proposal 2: if Proposal 1 is not agreed, RAN to task RAN1 to identify pros and cons of having the information on the number of Rx branches supported by a RedCap UE within the early indication during the initial access for the purpose of RACH procedure efficiency; RAN1 will then liaise with RAN2 so that RAN2 agreement from RAN2#104-e meeting can be revisited accordingly (if needed)

## Slide 6: References
[1] RP-210918, Revised WID on support of reduced capability NR devices, Nokia, Ericsson, RAN#91-e, March 22nd - 26th, 2021
[2] 3GPP RAN1#104b-e Chairman’s Notes, April 12th - April 20th, 2021 [link]
[3] R2-2106472, Report from Break-out session on R17 NTN and REDCAP, 3GPP RAN2#114-e, May 19th – 27th, 2021
[4] TR 38.875, Study on support of reduced capability NR devices, Rel-17
[5] R2-2105235, Early indication & access restriction for RedCap UEs, Ericsson, 3GPP RAN2#114-e, May 19th – 27th, 2021