## Slide 1: Views on postponed RAN4 RRM issues
MediaTek Inc.
3GPP TSG RAN 92E RP-211461
June 14-18 2021 Agenda Item 9.7.4

## Slide 2: Background
In RAN4#99e meetings, several RRM issues were decided to be postponed to Rel-17.
Issue | Document | Conclusion
NeedForGap measurement | R4-2108039 | Decision: Noted Session chair: There is no consensus to do the work in Rel-16 TEI due to potentially larger scope and late stage of Rel-16. The WF is agreeable to RAN4 and provides a set of candidate objectives. WF is noted as no work is planned. Further discussion in the plenary is recommended on whether and how to handle this.
MRTD for FR1 intra-band non-contiguous NR-CA/NR-DC | R4-2108221 | Decision: Noted Session chair: There is no consensus to do the work in Rel-16 TEI due to potentially larger scope and late stage of Rel-16. The WF is agreeable to RAN4 and provides a set of candidate objectives. WF is noted as no work is planned. Further discussion in the plenary is recommended on whether and how to handle this.
Per-FR gap capability | R4-2108332 | Decision: Noted Session chair: no consensus to define capabilities Agreements: Do not introduce per-BC indication of per-FR measurement gap UE capabilities in Rel-16. RAN4 has a common understanding that further enhancements to the per-FR measurement gap UE capabilities to address UE implementation constraints can be further studied in future (e.g. in Rel-17) and the work is subject to RAN plenary approval and available time budget.

## Slide 3: RAN4 workload issue
RAN4 workload is a recurring issue.
  Even in RAN4#99e (the 3rd meeting of Rel-17), Rel-16 issues are still prioritized in the RRM GTW session.
Proposal 1: Whether to start the RAN4 discussions for additional topics should also take into account the current RAN4 workload assessment from RAN4 chairman.

## Slide 4: NeedForGap measurement
Background
  NeedForGap signaling has been introduced in RAN2 TEI without RAN4 requirement.
  An important feature to avoid configuring measurement gap for inter-frequency measurements which lead to some throughput dropping.
Relation to ongoing NCSG discussion in Rel-17 NR_MG_enh
  Both are solutions for gapless measurement which utilizes UE’s spare RF chain(s).
    NCSG: Both network and UE has common understanding on the timing of interruption.
    NeedForGap: Whether to allow interruption is FFS.
  Besides interruption, other requirements like CSSF, measurement delay, impact to L1 measurements, scheduling restriction and UE capability report are expected be similar between these 2 features.
  Parallel/independent discussions for these 2 features may lead to an unnecessary increase of RAN4 workload as well inconsistent conclusions, and should be avoided.
Proposal 2: Subjected to RAN4 workload, merge NeedForGap requirements into NCSG in Rel-17 NR_MG_enh and increase the TU allocation by to 1.5 per meeting.

## Slide 5: MRTD for FR1 intra-band non-contiguous NR-CA/NR-DC
Background
  This issue was discussed in RP#89 meeting but was not agreed to be one of the Rel-17 NR_RRM_enh2 objectives.
  In later Plenary and RAN4 meetings, this issue was brought again without reaching conclusions.
Scope of the work
  As addressed in WF R4-2108221, this is not a pure RAN4 RRM work.
    RF session to conclude the UE and BS RF architecture first.
    RRM session to define the corresponding MRTD/MTTD requirement
    Demod session to define the PDSCH test case under the power imbalance agreed in RF session
  Since 3 phases are needed (RF  RRM  Demod), TEI is not a suitable place to have this discussion. In our view, a new (or existing) RF WI is better to start this discussion.
Proposal 3: Subject to RAN4 workload, the requirements for FR1 intra-band non-contiguous NR-CA/NR-DC are to be included in a new (or existing) RF WI with RRM and Demod objectives.

## Slide 6: Per-FR gap capability
Background
  Per-FR gap capability was introduced in Rel-15 and is per-UE reported.
  Some UE vendors have concern on the way it is reported, and suggest to add an new per-BC capability for it.
  This issue has been discussed in the feature list for 3 RAN4 meetings. The conclusions in RAN4#99e meeting are
    Do not introduce per-BC indication of per-FR gap UE capabilities in Rel-16
    FFS in future, subject to RAN plenary decision.
Expected additional workload
  RAN4: a scan of TS36.133 and TS38.133 requirements to identify the impact of new per-BC UE capability
  RAN2: add new per-BC capability.
  Both are expected to be done in one quarter.
Proposal 4: Subject to RAN4 workload, create a new RAN4 TEI to introduce per-BC indication of per-FR gap.

## Slide 7: Conclusions
Proposal 1: Whether to start the RAN4 discussions for additional topics should also take into account the current RAN4 workload assessment from RAN4 chairman.
Proposal 2: Subject to RAN4 workload, merge NeedForGap requirements into NCSG in Rel-17 NR_MG_enh and increase the TU allocation by to 1.5 per meeting.
Proposal 3: Subject to RAN4 workload, the requirements for FR1 intra-band non-contiguous NR-CA/NR-DC are to be included in a new (or existing) RF WI with RRM and Demod objectives.
Proposal 4: Subject to RAN4 workload, create a new RAN4 TEI for introducing per-BC indication of per-FR gap.

## Slide 8: Thank You!