## Slide 1: Discussion on introduction of new UE categories with 1 Rx based on Category 3 and 4 for LTE
3GPP TSG RAN Meeting #92-e
Electronic Meeting, June 14th – 18th, 2021
Document for: Approval
Agenda Item: 10.11
Source: CAICT, China Telecom, China Unicom, Guangdong Genius, Honor, Huawei, HiSilicon, OPPO, Samsung, Spreadtrum, vivo, Xiaomi
RP-211466

## Slide 2
Background
In Rel-14 the new UE DL category 1bis (Cat 1bis) was introduced for wearable device with single antenna based on UE category 1 [1].
  The new RF, RRM and performance requirements are specified for Cat 1bis to verify the single Rx antenna performance in TS 36.101 and TS 36.133 (RAN4)
  The new DL category 1bis is specified in TS 36.306 and TS 36.331 (RAN2)
The urgent market need is observed for high-end wearable devices, e.g., smart watches. The data rate of this device cannot be met by LTE Category 1bis. At the same time due to form factor reasons such wearable devices would require the single Rx, which cannot be supported by LTE Category 3 and 4.

## Slide 3
Discussion-1
To meet high-end wearable device market demand, the new UE DL categories with single Rx antenna and support of higher throughput than LTE Cat 1bis need to be defined from Rel-17. Possibility for early implementation should be discussed.
The new DL categories with single Rx antenna based on Category 3 and Category 4 could be considered.
Proposal 1: Define new LTE UE DL category 3bis and 4bis with single Rx antenna based on UE category 3 and 4.

## Slide 4
Discussion-2
The work can be minimized by using the framework which has already been established for Cat 1bis and most of RAN4 requirements for Cat 1bis except for peak data rate test
  Reuse the existing RF, RRM and performance requirements specified for Cat 1bis as much as possible for LTE Cat 3bis and Cat 4bis
  Specify additional SDR (Sustained DL Data Rate) tests to verify the peak data rate for new DL categories
  Complete the above work within one quarter by TEI-17
Proposal 2: For LTE Cat 3bis and Cat 4bis, reuse the existing RF, RRM and performance requirements specified for DL 1bis to verify single Rx antenna performance, and add additional SDR tests to verify the peak date rate.
Proposal 3: Task RAN2 and RAN4 to finalize work for LTE Cat 3bis and Cat 4bis in TEI17

## Slide 5
Reference
[1] RP-170791, Revised WID: Requirements for a new UE category with single receiver based on Category 1 for LTE, Qualcomm