## Slide 1
3GPP TSG RAN Meeting #93e RP-211793
Electronic Meeting, September 13-17, 2021
Agenda item : 9.0.2
Source : Samsung
Title : View on the scope of Rel-18 Advanced MIMO for NR
Document for : Discussion and Decision

## Slide 2: Background | Latest categorization for DL MIMO and UL [RWS-210659] (RAN1 led)
1. Evolution for downlink MIMO, with the following example areas:
  Further enhancements for CSI (e.g., mobility, overhead, etc.)
  Evolved handling of multi-TRP (Transmission Reception Points) and multi-beam
  CPE(customer premises equipment)-specific considerations
2. Uplink enhancements, with the following example areas:
  >4 Tx operation
  Enhanced multi-panel/multi-TRP uplink operation
  Frequency-selective precoding
  Further coverage enhancements
While UL enhancements include some UL MIMO components, the contribution will focus on item 1 (evolution for downlink MIMO)

## Slide 3: Background |Outcome of email discussion – DL MIMO
For Example Area 1 - Further enhancements for CSI (e.g., mobility, overhead, etc.), further discussion could focus on following items:
  Enhancement for high/medium mobility, (Not controversial in framework), including, e.g.,
    Time-domain correlation/doppler-domain based CSI feedback or overhead reduction (Controversial)
  Enhancement of CSI acquisition for TDD via SRS enhancement (Controversial)
  Enhancement for M-TRP URLLC (Controversial)
For Example Area 2 - Evolved handling of multi-TRP (Transmission Reception Points) and multi-beam, further discussion could focus on following items:
  Extend Rel-17 Unified TCI framework, e.g.,
    for indication of multiple DL and UL TCI states (e.g., M>1 and/or N>1, and [inter-band]) (Not controversial in framework)
    Combined MTRP schemes, more generic (Controversial)
  Increasing the number of orthogonal DL [and UL] DMRS ports both for S-TRP and M-TRP (Not controversial in framework)
  Enhancement for Coherent-JT/D-MIMO, including e.g., codebook, CSI reporting, spatial domain interference avoidance (Controversial)
  Overhead and/or Latency reduction for beam management procedure/beam acquisition procedures, more generic (Controversial)
  Asynchronous M-TRP/Multiple TA for M-TRP (Controversial)
For Example Area 3 - CPE (customer premises equipment)-specific considerations, further discussion could focus on:
  Priority of CPE: Lower Pority (Controversial)
For "UL Related" area, which is raised in this week, Moderator lists all related schemes below for reference, and would like to propose to suspend the discussion at this moment, waiting for the decision on the umbrella for UL part.

## Slide 4: Assessment on conclusion of email discussion | Example area 1
#1: Study phase is needed before committing to specification work
  Scenarios of interest need to be identified first
  Several candidate frameworks are available and need to be compared – including potential enhancement on CSI-RS to enable estimation of time- or Doppler-domain correlation
  Potential benefit may very depending on the chosen framework
#2: SRS design enhancement is typically not considered as CSI enhancement
  The goal of this item (as in the summary) is unclear (e.g. for high/medium mobility, or other purposes such as C-JT)
  If this is for high/medium mobility, Example Area 1 should also include potential enhancements beyond CSI
  Regardless, study phase is also needed
#3: The scope of CSI enhancement for mTRP URLLC is unclear
  Extensive discussion has taken place in Rel-17 URLLC WID – concluded with enhancing differential CQI
  Unclear what is needed beyond Rel-17 enhancement. Some examples may help, e.g. faster A-CSI triggering? A-CSI for initial access? DMRS-based CQI?
For Example Area 1 - Further enhancements for CSI (e.g., mobility, overhead, etc.), further discussion could focus on following items:
Enhancement for high/medium mobility, (Not controversial in framework), including, e.g.,
  Time-domain correlation/doppler-domain based CSI feedback or overhead reduction (Controversial)
Enhancement of CSI acquisition for TDD via SRS enhancement (Controversial)
Enhancement for M-TRP URLLC (Controversial)

## Slide 5: Assessment on conclusion of email discussion | Example area 2
#1: Due to lack of time in Rel-17, this feature is postponed to Rel-18 (hence needs to be specified)
  However, “Combined mTRP schemes, more generic” should be removed since the scope is unclear
    Proposal to allow mixture between m-DCI and s-DCI for m-TRP can be handled via NW implementation once indication of multiple TCI states is supported. Other proposals mentioned in the email discussion don’t correlate strongly with m-TRP
#2: We are fine with the description
#3: Support from a number of operators
  Improving spectral efficiency especially for sub-1GHz FDD and FR1 TDD deployments
  In addition to CSI, SRS enhancement targeting this scenario should be included
For Example Area 2 - Evolved handling of multi-TRP (Transmission Reception Points) and multi-beam, further discussion could focus on following items:
Extend Rel-17 Unified TCI framework, e.g.,
  for indication of multiple DL and UL TCI states (e.g., M>1 and/or N>1, and [inter-band]) (Not controversial in framework)
  Combined MTRP schemes, more generic (Controversial)
Increasing the number of orthogonal DL [and UL] DMRS ports both for S-TRP and M-TRP (Not controversial in framework)
Enhancement for Coherent-JT/D-MIMO, including e.g., codebook, CSI reporting, spatial domain interference avoidance (Controversial)
Overhead and/or Latency reduction for beam management procedure/beam acquisition procedures, more generic (Controversial)
Asynchronous M-TRP/Multiple TA for M-TRP (Controversial)

## Slide 6: Assessment on conclusion of email discussion | Example area 2
#4: Studied in Rel-17, most likely not enough time to specify and can be done in Rel-18
  Beneficial to improve efficiency at high UE speed and/or large # configured TCI states
  Continue from the study outcome of Rel-17
  Scope should be described clearly, e.g. UE-initiated beam management, beam refinement/tracking, via down selection and benefit assessment, hence some study phase is needed
#5: Discussed in Rel-17 but no consensus to support
  Relaxing inter-TRP DL timing offset requirement is beneficial to improve utility of mTRP especially for FR2
  Support of multiple TA is more UL-related than DL, therefore should be moved under UL enhancement
  As this item was controversial in Rel-17, it may benefit from some study phase as well, e.g. impact of relaxing DL timing assumption (also involving RAN4)
For Example Area 2 - Evolved handling of multi-TRP (Transmission Reception Points) and multi-beam, further discussion could focus on following items:
Extend Rel-17 Unified TCI framework, e.g.,
  for indication of multiple DL and UL TCI states (e.g., M>1 and/or N>1, and [inter-band]) (Not controversial in framework)
  Combined MTRP schemes, more generic (Controversial)
Increasing the number of orthogonal DL [and UL] DMRS ports both for S-TRP and M-TRP (Not controversial in framework)
Enhancement for Coherent-JT/D-MIMO, including e.g., codebook, CSI reporting, spatial domain interference avoidance (Controversial)
Overhead and/or Latency reduction for beam management procedure/beam acquisition procedures, more generic (Controversial)
Asynchronous M-TRP/Multiple TA for M-TRP (Controversial)

## Slide 7: Assessment on conclusion of email discussion | Other
Example area 3 can be assigned a lower priority
UL-related areas such as UL TPMI, >4Tx UL, UL multi-panel, and multiple TA to support mTRP can be included as a part of UL enhancement discussion
For Example Area 3 - CPE (customer premises equipment)-specific considerations, further discussion could focus on:
  Priority of CPE: Lower Pority (Controversial)
For "UL Related" area, which is raised in this week, Moderator lists all related schemes below for reference, and would like to propose to suspend the discussion at this moment, waiting for the decision on the umbrella for UL part.

## Slide 8: C-JT with distributed RRH | Motivation and Scope
Facilitate deployments with multiple RRH or Active Antenna modules
  Especially targeting low frequency FR1 bands (sub-1GHz) FDD, also FR1 bands TDD
    Capacity/coverage limitation for sub-1GHz (form factor limitation at gNB)
  Study on assumptions and channel modeling seems needed (for the first, e.g., 2 meetings)
Potential enhancement/study areas:
  New CSI codebook(s) accommodating largely-spaced RRHs (possibly with different # of ports) and the necessary CSI reporting with >32 ports, including for (if required) UE-assisted calibration
  RS enhancement to enable >32 ports and >8 layers for both FDD and TDD – mindful of overhead
  New (interference) measurement for enabling dynamic RRH selection
Distributed/Multi-panel FD-MIMO
64T64R for 700MHz???
4x 4T4R
4x 4T4R
4x 4T4R
4x 4T4R
INFEASIBLE
UE
Multiple RRH
Single-panel FD-MIMO

## Slide 9: C-JT with distributed RRH | Performance gain
700MHz band, 10MHz system bandwidth, RMa 1.7km ISD, MU-MIMO with 2-RX UEs, FTP-1 traffic, FDD
  CB1: eType-II per RRH
  CB2: Modified eType-II (SD per RRH, FD across RRHs)
Chart: Avg UPT Gain
| CMIMO,16ports,CB | CMIMO,16ports,ideal | DMIMO,8ports,pwrAdjOff,CB | DMIMO,8ports,pwrAdjOff,CB2 | DMIMO,8ports,pwrAdjOn,ideal
 | 100 | 103.3703 | 108.1944 | 120.4144 | 127.5196
(%)
8%
20%
C-MIMO Ideal CSI
D-MIMO CB1
D-MIMO Ideal CSI
D-MIMO CB2
27%
C-MIMO CB (Rel-16 Type-II)
Chart: Avg UPT Gain
| CMIMO,8ports,CB | CMIMO,8ports,ideal | DMIMO,16ports,pwrAdjOff,CB | DMIMO,16ports,pwrAdjOff,CB2 | DMIMO,16ports,pwrAdjOff,ideal
 | 100 | 103.5602 | 134.3928 | 143.2275 | 147.7849
(%)
34%
43%
C-MIMO CB (Rel-16 Type-II)
C-MIMO Ideal CSI
D-MIMO CB1
D-MIMO Ideal CSI
D-MIMO CB2
48%
- Scenario #1
- Scenario #2

## Slide 10: Proposal |
On Rel-18 DL MIMO enhancement, include example areas 1 and 2 from the moderator conclusion with the following refinement
  Area 1:
    Designated “Perform study and, if needed, specify”
    CSI for mTRP URLLC needs to be clearly defined in terms of goal and scope, else should be removed
  Area 2:
    ‘Extend Rel-17 unified TCI framework’ is designated “Specify” with ‘Combined mTRP schemes’ removed
    Orthogonal DMRS enhancement is designated “Specify”
    C-JT enhancement is designated “Specify” with SRS enhancement for TDD CSI acquisition included
    Overhead/latency reduction for BM is designated “Perform study and, if needed, specify” and needs more specific description to avoid indefinite scope
    Asynchronous mTRP is designated “Perform study and, if needed, specify” to assess the extent of enhancement, but move ‘multiple TA’ to UL enhancement
Proposed WID for Rel-18 DL MIMO enhancement is given in RP-211792