## Slide 1: Motivation for NR Passive IoT for automotive industry
CMCC, BMW Brilliance Automotive
3GPP TSG RAN Meeting #93-e RP-211990
Electronic Meeting, September 13 - 17, 2021

## Slide 2
Overview--Use Cases for Automotive Industry
After field trial, we observed the above use cases marked with RED CANNOT be met by current 5G specification, which need further enhancement in Rel-18, including the support for perception and positioning of materials.
PTL Trolley
Machine Vision
Welding group control
5G Networking AGV
Automobile assembly workshop
Data center
Robot Control
5G could solve frequent Wi-Fi disconnection causes information loss and system confusion.
PTL trolley communication is 10 times/minute. Single-vehicle, 1000 square meters, 200 concurrent requests per minute, Wi-Fi cannot meet large concurrency requirements.
MCU Software 5G Loading
5G can provide software download for 100 vehicles at the same time, eliminating up to one hour of loading time and eliminating space consumption for centralized parking of vehicles.
Dozens of network cables between the 5G welding control cabinet and computer
5G Substitutes Wired for Low-Latency Control of Robotic Arm and Flexible Deployment
5G supports remote upgrade and maintenance.
NLOS Positioning
Perception
multiple inbound and outbound crossings、asset stocktaking
Logistics Management 、vehicle positioning in product line
Red
The above use cases marked with GREEN can be met by current 5G specification.
Green
5G can address several use cases, but some use cases (Perception and Positioning) still need to be further enhanced to meet the requirement from automotive industry.

## Slide 3
Passive IoT enabled Perception
RFID was considered, but has the following drawbacks:
Bad performance: Based on our test, RFID can only read labels in case the labels are not blocked. On the other words, in case the label attached on the bin is blocked, e.g. by another metal bin, RFID always fails to read it.
High Cost: The transmission distance for RFID readers is short, about 8 meters based on test. We need to deploy a lot of RFID readers to cover the whole warehouse(about 5000m2). Therefore, the cost to deploy the readers is very high.
Bin management at the Gate of the warehouse
Scenario: unique identify the bins for logistic management. E.g.
Identify which bins move in or out of the warehouse, at the Gate of the warehouse.
Identify the bins in a specific area inside the warehouse.
Currently, bins are manually managed via scanning the barcode attached on each bin.
Causes：
High OPEX: OPEX of warehouse management is very high for us;
Manual error: Manual work often cause errors and many bins lost;
We are considering Automatic bin Management in the warehouse with a quite low cost.
Use cases
Bin management inside the warehouse

## Slide 4
Passive IoT enabled Perception
Coverage capability: communication distance should be enhanced to 30 meters to construct a feasible network coverage in the 5000 m2 warehouse.
UE power consumption: <0.1mW to support working without battery.
UE cost: <0.1￥(~0.02$) to meet cost-sensitive applications.
Positioning accuracy： 3~5m(Horizontal&Vertical) @ 90% for positioning .
There is no battery in the terminal and the terminal accumulate the energy from radio signaling. Additionally, the terminal may also accumulate energy from solar energy as supplement.
Key Requirements for Passive IoT
What is Passive IoT

## Slide 5
Potential Standardization work for Passive IoT
Passive IoT Tag
5GC
Passive IoT Server
NR
RAN Group
Motivation: study and develop the air technology to support the batteryless IoT device.
RAN Work scope:
  Requirements and performance assessment
  Downlink coding and modulation
  Uplink coding and modulation scheme supporting backscatter transmission
  Frame structure and synchronization scheme
  Minimized protocol stack and signalling
  Coexistence with existing cellular technologies in licensed spectrum
SA2 Group
Motivation: study and develop the network architecture to support batteryless IoT device and enable the business.
SA2 Work scope:
  Study the general architecture for supporting Passive IoT in 5G system
  Study how to manage the Passive IoT device
  Study how to manage the connectivity for the Passive IoT device
  Study how to support the mobility for Passive IoT device

## Slide 6
Thank You