## Slide 1
3GPP TSG RAN 93e RP-212018
Electronic Meeting, Sep. 13th-17th, 2021
Source: vivo
Document for: Discussion & Decision
Agenda Item: 9.0.3
Further CADC enhancements in Rel-18

## Slide 2
Flexibility aggregation for Multiple carrier
SUL in NR and Diverse Spectrum in NR
Observation1: Scattered narrow band in NR is hard to be used for idle UE e.g. sending SIBx. we think allowing random access on the non-anchor carrier is beneficial to avoid the congestion issue on the anchor carrier.
Proposal1: Anchor carrier can be introduced for idle UE, paging and SIBx are transmitted only in anchor carrier.
Observation2: The SSB-less Scell as commented by some companies during the pre-email discussion can be reused here to reduce the SSB/Paging/SIB transmisison on the non-anchor carrier but it also prevents the UE random access on these carriers, therefore some enhancements would be needed.

## Slide 3
Background
  RAN1 work on two-cell PDSCH scheduling via a single DCI for specification support in Rel-17 DSS is stopped due to Rel-17 WID scope only focusing on two DL carriers within FR1, RAN1 did not study the potential benefits for more than 2 carriers for both UL and DL within FR1 and FR2.
  There is a potential to further improve NR DL/UL capacity or resolve scheduling limit in CA due to BD/CE budget in some specific scenarios, e.g., in higher frequency, in intra-band CA, by using the feature of single DCI scheduling multiple DL/UL transmission
Proposal2: Study, and if agreed specify PDCCH of P(S)Cell/SCell scheduling PDSCH/PUSCH on multiple cells using a single DCI within FR1 and FR2
MRDC
Multi-cell scheduling

## Slide 4
Fast activation
Fast SN switching/activation
Observation1: always RRC reconfiguration for SN change is low efficiency for MR-DC in small cell case
Proposal3: Fast SN Switching/activation should be specify when Multi-SN can be configured for the UE.
Note1: Only two TX transmissions are allowed at same time

## Slide 5
  Fast SN switching/activation when Multi-SN can be configured for the UE
    Fast SN switching/activation CP and UP architecture enhancement for MR-MC, e.g. new SRB and DRB
    MN and SN initialize secondary SN addition/change/release.
    Lower layer signaling to activate and deactivate SNs.
    Note1: Only two TX transmissions are allowed at same time
Improved multi-carrier operation
  Study to introduce anchor carrier to Scattered narrow band usage in NR for idle UE.
  Study, and if agreed specify PDCCH of P(S)Cell/SCell scheduling PDSCH/PUSCH on multiple cells using a single DCI for FR1 and FR2
CA/DC enhancement in R18
Scope