## Slide 1: Discussion on unlicensed spectrum for sidelink communication for Rel-18
5G Team / Lenovo Research / MBG
Agenda Item: 9.0.2
Source: Lenovo, Motorola Mobility
Document for: Discussion
3GPP TSG RAN Meeting #93-e RP-212066
Electronic Meeting, September 13 - 17, 2021

## Slide 2: Justification
  Wide bandwidth
  High data rate
  Latency reduction
  Traffic offloading
  Low cost
  Extended coverage
Motivation
Spectrum
  6GHz:
    US 5.925 – 7.125GHz
    EU 5.925 – 6.425GHz
  60GHz:
      US 57GHz – 71GHz
      EU 57GHz – 66GHz
Study in 3GPP
  LTE Rel-13 LAA
  LTE Rel-14 eLAA
  LTE Rel-15 FeLAA
  NR Rel-16 NR-U
  NR Rel-17 Above 52.6

## Slide 3: Operation scenarios
Scenario 1: intra-cell in coverage
Scenario 2: inter-cell in coverage
Scenario 3: partial coverage
Scenario 4: out of coverage

## Slide 4: Objectives
Waveform design to meet OCB and PSD requirements
  PSCCH
  PSSCH
  PSFCH
SCI format design
DRS window containing at least SL SSBs, PSBCH and possibly CSI-RS with properties and extensions to handle reduced SSB and RMSI transmission opportunities due to LBT failure.
Physical layer channels and signals
Resource allocation based on scheduling and sensing
UE-to-UE COT sharing among Tx UE and Rx UE for simple channel access
Channel access mechanism for fair coexistence
Synchronization procedure
Scheduling/HARQ
Multi-carrier support (carrier aggregation, carrier duplication)
Physical layer procedures
Radio interface protocol architecture and procedures
  Relevant protocol and procedure enhancements (e.g., RRC and MAC) to support service continuity on unlicensed spectrum.