## Slide 1
Agenda Item: 9.0.4
Source: Samsung
Title: On AI for NG-RAN in Rel-18
Document for: Discussion
RP-212073
3GPP TSG RAN Meeting #93e
Electronic Meeting, September 13 - 17, 2021
SAMSUNG

## Slide 2: AI for NG-RAN | Overview and Structure
Status of Rel-17 SI: FS_NR_ENDC_data_collect
  AL/ML framework, some high level principles and definitions were agreed.
  Use cases agreed to study: load balancing, energy saving, mobility optimization/traffic steering
  Some specification impacts have been identified for the three use cases
  RAN3 will continue to study the specifications impacts before considering any new use cases.
  Observation 1: The AI/ML-based load balancing, energy saving and mobility optimization need to be supported by normative work in Rel-18 WI based on the outcome of the RAN3 study in Rel-17 RAN3 SI. The detail scope of the Rel-18 AI/ML for NG-RAN WI can be defined when the SI is finalized.
  Observation 2: No new use case could be discussed in the ongoing Rel-17 SI FS_NR_ENDC_data_collect.
During the email discussion before RAN#93e, the moderator has proposed the project structure for NG-RAN:
  AI for NG-RAN WI (RAN3 lead, secondary WG: RAN2)
  SI on additional use cases on AI/ML for NG-RAN (RAN3 lead)
We fully agree with this AI/ML project structure for NG-RAN considering the status of the Rel-17 SI. This is inline with our observations.
Proposal 1: Agree to have a Rel-18 WI on AI for NG-RAN to include the conclusion of the Rel-17 SI and a separate Rel-18 SI to study the additional use cases.
Proposal 2: The scope of the Rel-18 AI/ML for NG-RAN WI can be defined when the SI is finalized.

## Slide 3: AI for NG-RAN SI| Use case #1: Mobility enhancement
DC related mobility cases will not be considered in the ongoing Rel-17 SI. As a mechanism to improve throughput and reliability, DC related mobility requires to enhance robustness and efficiency.
  High complexity to decide the handover type due to multi-dimensionality HO, e.g. CPAC, single-connectivity to dual-connectivity handover, DC to single-connectivity handover, inter-MN handover without SN change, SN change.
  Heavy overhead and performance downgrading brought by unsuitable HO policy/decision
  Lack of precise solution for failure detection during DC related procedures
Possible AI/ML-based mobility enhancement:
  Important parameters prediction for HO policy/decision: e.g. traffic, QoS performance predication to assist HO policy setting.
  Decision based predication: predicated handover policy for dual-connectivity case to improve HO robustness and efficiency.
Proposal 3: Mobility enhancement is a potential use case for RAN intelligence to improve mobility robustness and efficiency for dual-connectivity scenarios.
AI Model
1. Input data
2. Predicted parameters or policy
Node 3
Node 1 (MN)
Node 2 (SN)
3. SN addition request

## Slide 4: AI for NG-RAN SI| Use case #2: Slicing
Slicing is paradigm to support services with highly diverse QoS via separating resources within a common infrastructure.
  Fluctuations in traffic demand weaken the effect of resource allocation policy, resulting in large overhead for re-configuration.
  Network uncertainty (e.g. load, etc.) and delayed reconfiguration may deteriorate the QoS performance or the spectrum efficiency.
Possible AI/ML-based slicing:
  Resource allocation: set proper resource allocation and remapping policy for slices to improve the slice resource efficiency and satisfy QoS of UEs.
Proposal 4: Slicing is a potential use case for RAN intelligence to achieve the trade-off between resource efficiency and Qos performance.
AI Model
Predicted parameters or policy
RAN
CN
Input data
AI Model
Slice 1
Slice 2
Slice 3
Input data
Predicted parameters or policy

## Slide 5: AI for NG-RAN SI| Use case #3: IAB
IAB as a new feature for 5G is to extend the coverage via multi-hop, while guaranteeing robustness and load balance.
  Topology management, route selection and switching, resource allocation across multiple nodes become complex in IAB network
  Multi-objective optimization is a heavy task for conventional way to generate proper policy timely.
Possible AI/ML-based IAB:
  Resource usage prediction: predict node resource usage to foresee the impact brought by new traffic.
  Routing: set adaptive routing policy to achieve joint optimization of coverage, robustness and load balance.
Proposal 5: IAB is a potential use case for RAN intelligence to realize joint optimization of coverage, robustness and load balance.
IAB donor (gNB)
IAB node
IAB node
AI Model
Input data
Predicted parameters or policy

## Slide 6: AI for NG-RAN SI| Use case: Others
Other possible use cases to be studied e.g. QoE, URLLC
  QoE.
    relationship between QoE parameters and network related parameters (e.g. QoS) is not explicit.
    QoE prediction: predict the varying-trend of QoE for maintaining user experience
  URLLC
    Resource allocation: AI powered optimized resource allocation policy with high resiliency to variations.
    PDCP duplication: dynamic path selection to meet QoS requirement with minimum resource
Proposal 6: Other possible use cases to be studied e.g. QoE, URLLC if time allows

## Slide 7: AI for NG-RAN | Proposals
Based our analysis, the following were proposed on AI for NG-RAN in Rel-18
  Proposal 1: Agree to have a Rel-18 WI on AI for NG-RAN to include the conclusion of the Rel-17 SI and a separate Rel-18 SI to study the additional use cases.
  Proposal 2: The scope of the Rel-18 AI/ML for NG-RAN WI can be defined when the SI is finalized.
  Proposal 3: Mobility enhancement is a potential use case for RAN intelligence to improve mobility robustness and efficiency for dual-connectivity scenarios.
  Proposal 4: Slicing is a potential use case for RAN intelligence to achieve the trade-off between resource efficiency and Qos performance.
  Proposal 5: IAB is a potential use case for RAN intelligence to realize joint optimization of coverage, robustness and load balance.
  Proposal 6: Other possible use cases to be studied e.g. QoE, URLLC if time allows

## Slide 8
Thank you