## Slide 1: Handling of SIP signaling coverage issue identified in Coverage Enhancement SI/WI
SoftBank, Verizon, Ericsson
3GPP TSG RAN Meeting #93-e
Electronic Meeting, September 13 - 17, 2021
Agenda Item: 9.3.1.5
Document for: Discussion and Decision
RP-212095

## Slide 2: Background 1
In Coverage Enhancement SI, an issue related to SIP signaling was pointed out, which has been well known in 3GPP, especially RAN2
  Quote from TR36.754 below
    Size of SIP message used in VoLTE call setup is about 2KB. When UE is in poor radio condition (e.g. RSRP < - 120dBm) and/or high interference (e.g. uplink IoT = 10dB), it has been observed in practical network that a SIP message is segmented into 200 RLC pieces, thus average call setup time and call drop rate are increased. Therefore a large SIP message size becomes a problem.
  Further analysis on this issue is found in R1-2003464
It is also acknowledged through the SI that the following solution can be potentially taken to address this issue
  Enhancements on container physical channel, i.e. PUSCH
    RAN1 is now working on the general PUSCH enhancements
    Gain of several dB is expected, which is not enough to convey big data such as SIP signaling
  Introduction of compression scheme(s)
    UDC – RAN level compression (to be specified in Rel-17)
    SigComp – Application level compression
This issue should be solved before VoNR service enters into market
  Latency of call setup is a clear disadvantage compared with OTT voice application
Considering the fact that SIP signaling is unnecessarily redundant, use of compression scheme is quite reasonable and efficient.

## Slide 3: Background 2
Applicability of higher layer compression scheme(s) has been left untouched so far because CovEnh WI is led by RAN1
  Interpretation 1: UDC can compress SIP signaling. Thus, UDC and solve this issue and no further clarification of CovEnh WID is necessary
  Interpretation 2: UDC CANNOT compress SIP signaling in the case where encryption is applied (e.g. IPSec). Thus SigComp needs to be mandatorily used
    See "R1-2107564“ for more detail
While UDC is going to be specified, but use of SigComp is potentially only way for SIP compression considering the usage of IPSec between UE and IMS
  It does not make any sense to disable encryption for the purpose of SIP compression
The source companies believe SIP signaling issue shall be solved in Rel-17 timeline
  RAN is required to give a proper guidance to the appropriate WGs to accelerate the discussions

## Slide 4: Proposal
RAN to address SIP signaling coverage issue by e.g., compression approach
RAN to send a LS to CT1, SA4 and cc SA2:
  To indicate that 2KB SIP message sizes may impact VoNR coverage or setup latency in arduous coverage scenarios, and
  To check if SigComp functionality can be mandated to reduce SIP message overhead