## Slide 1: Motivation on HAPS study
SoftBank
3GPP TSG RAN Meeting #93-e
Electronic Meeting, September 13 - 17, 2021
Agenda Item: 9.0.2
Document for: Discussion and Decision
RP-212099

## Slide 2: Background
HAPS is one of the most important future technologies to achieve wide coverage with reasonable cost.
  The reports on flight/connectivity tests are going to be published(see Annex), which reveals that HAPS is real.
  However, satellite is commercially advanced, and a greater number of companies showed their interests than that of HAPS.
HAPS has notable benefits over other NTN technologies
  Examples:
    Less necessity of addressing the issues on doppler shift and/or round-trip delay, no additional essential functionalities are required on top of TN
    The available spectra for HAPS can be identical to (or part of) terrestrial ones, i.e. no additional band support is necessary.
    Regenerative payload is the baseline, i.e. inter-HAPS coordination can be available
  However, this kind of difference was vanished due to the implicit-support manner.
    The focus of Rel-17 is to overcome doppler shift and round-trip delay
These result in no specific work in Rel-16 and 17, i.e. HAPS was treated as an “implicit support”
No deployment scenario(s) defined in TR38.821
No evaluation efforts except RAN4 co-ex study
No specific features for HAPS in Rel-17
Many sentences in TR38.821 applicable to Satellite only, i.e. unclear or not true for HAPS
Now NTN is going to enter optimization phase in Rel-18. Satellites (LEO, MEO, GEO) are ready for optimization, but HAPS is not due to the lack of sufficient study so far.

## Slide 3: Problems on the current TR from HAPS point of view
Section 4.2
  Inappropriate wording: “One ISL case and one without ISL. Regenerative payload is mandatory in the case of inter-satellite links.” is not appropriate in order to equally prioritize HAPS in this TR.
  No HAPS description in the Reference scenarios (Table 4.2-1) and its corresponding parameters (Table 4.2-2)
Section 5.2
  Inappropriate section name: This should not be restricted to “satellite”.
  Also “Satellite” in used in many places in this section, which needs to be corrected to include UAS/HAPS to avoid the misreading
    SRI should be “satellite or UAS Radio Interface” or something similar, and
    Similar collection is needed for ISL, etc
  Completion of section 5.2.3 (applicability of IAB) is desired given inter-HAPS link is attractive
Section 5.4
  No support of co-channel scenario (i.e. use overlapping spectrum for TN and NTN)
Section 6
  HAPS scenarios are missing in tables 6.1.1.1-X (X is arbitrary applicable value(s))
Section 7
  HAPS scenarios are not captured in Table 7.1-1
  TDD is down-prioritized in the original study while TDD is still applicable for HAPS
  No study on mobility issues for HAPS in 7.3.2.
  Analyses on ephemeris data is performed from satellite only in 7.3.6 while it is also useful for HAPS

## Slide 4: Proposal
Approve at least the following scope in Rel-18 to improve the visibility of 3GPP activities for HAPS
  Development of HAPS deployment and configuration scenario(s), which are not studied and missing in TR38.821.

## Slide 5: Annex: information of HAPS feasibility
Technologies have already existed to deliver mobile connectivity from the stratosphere
  SoftBank’s HAPSMobile successfully conducted stratospheric flight and mobile communication test with its solar-powered UAS and stratosphere-ready communication payload.
    The test flight took place on September, 2020 at Spaceport America (“SpA”), New Mexico
    Using MIMO technology, the payload enabled LTE connectivity to be delivered continuously for approximately 15 hours during test flight.
    Communications payload enabled a video call with smartphones at SpA and HAPSMobile team members in Tokyo. The test system was composed of a service link using the 700MHz spectrum band (LTE Band28)
More detail can be found in the press release (https://www.hapsmobile.com/en/news/press/2020/20201008_01/)
  *HAPSMobile Inc. is a subsidiary of SoftBank Corp. and minority-owned by AeroVironment, Inc.