## Slide 1
Views on NR MBS evolution in Rel-18
3GPP TSG RAN Meeting #93e
Electronic Meeting, Sep 13 - Sep 17, 2021
Agenda item: 9.0.3
China Broadcasting Network Co. Ltd
RP-212145

## Slide 2: Background
NWM discussions (thread #9)
RP-211659 Moderator's summary for discussion [RAN93e-R18Prep-09] Evolution for broadcast and multicast services
Evolution of NR Multicast Broadcast Services
Objectives:
-(non-controversial) Rel-17 left-overs (content to be identified and detailed at end of Rel-17)
-(non-controversial) SFN support for MBS reception (above gNB-DU level)
-(controversial) based on which numerology
-(non-controversial) Support of Multicast INACTIVE state
-(controversial) Support of Multicast IDLE state
-(non-controversial) Enable Higher reliability, lower latency, larger coverage incl. improvement of spectrum
efficiency/capacity/reliability for NR MBS, Incl. RAN Sharing
-(controversial) Improve Energy efficient operation/power saving mechanisms for MBS reception
  Additional objectives:
  -(controversial) Public safety focused enhancements
  -(controversial) Support of Free-to-Air/receive only mode
(controversial) Additional Study on BMUST

## Slide 3: Rel-18 MBS: Support of Free-to-Air/receive only mode
Free-to-Air (FTA) broadcast is an essential feature to enable public services for NR MBS.FTA is crucial for CBN further nationwide 5G network deployment plan on spectrum which is designated for FTA public services in China. Innovative 5G-enabled public would be provided on such spectrum in a Free-to-Air manner throughout China covering 1.4 Billion people.
Potential enhancements for better FTA Broadcast support include, e.g. to provide UE capabilities to aid configurations for simultaneous unicast and FTA broadcast reception. The enhancements have limited impact on standards such as UE capability report and FTA reception status report.
Proposal: Given its importance and limited effort, necessary enhancements of FTA/ROM should be included as part of Rel-18 NR MBS evolution.

## Slide 4: Rel-18 MBS: Support of RAN Sharing
RAN sharing scenario refers to the same MBS service should be able to be identified as one unified service for all the relevant operators (rather than based on different TMGIs). RAN can use the same resources to schedule the same content for UE subscribing to different operators.
RAN sharing scenario is a real and important use case in practical deployment from operator point of view.
Proposal: “Improved MBS transmission efficiency in RAN sharing scenario” should be listed separately as one of the objective in the scope of Rel-18.

## Slide 5: Rel-18 MBS: Support of Multicast IDLE state
MBS use cases (e.g. Mission Critical services) have been identified to require support of very large UE numbers. It is not feasible to keep all devices connected. The number of UEs in the inactive state accommodated by the base station is still limited. Support of multicast in IDLE is therefore meaningful.
The extra effort in RAN to support multicast in idle is limited. SA is also considering taking this as part of
Rel-18. We do not see any reason to exclude this enhancement for Rel-18 from standardization effort
point of view.
Proposal: Multicast in both idle state and inactive state should be supported in the scope of Rel-18.

## Slide 6: Rel-18 MBS: Public safety focused enhancements
Government and public service entities have urgent demand for 5G-enabled innovative ways of
communicating with citizens. Multicast and Broadcast shall be adopted to more efficiently deliver real-
time emergency multi-media notifications to a wide variety of devices under the scope of public safety
(like disaster warning, security, pandemic control, etc.).
Proposal: Public safety focused enhancements should be included in the scope of Rel-18. The exact work scope can be further discussed.

## Slide 7: Summary
Proposal1: Given its importance and limited effort, necessary enhancements of FTA/ROM should be included as part of Rel-18 NR MBS evolution.
Proposal2: “Improved MBS transmission efficiency in RAN sharing scenario” should be listed separately as one of the objective in the scope of Rel-18.
Proposal3: Multicast in both idle state and inactive state should be supported in the scope of Rel-18.
Proposal4: Public safety focused enhancements should be included in the scope of Rel-18. The exact work scope can be further discussed.
Proposal5:Take “Evolution of NR Multicast Broadcast Services” as a WI alone and do not mix it with “Evolution of 5G LTE based broadcast”.