## Slide 1: Enhancing multi-carrier uplink operation in Rel-18
3GPP TSG RAN Meeting #93-e
Electronic Meeting, Sept 13 – 17, 2021
Document for: Approval
Agenda Item: 9.0.2
Source: Huawei, HiSilicon, CMCC, China Telecom, China Unicom, VIVO
RP-212149

## Slide 2
Background
RWS-210659 (RAN Rel-18 workshop summary) identified Uplink Enhancements as an important topic for release 18, with a list of example areas:
2. Uplink enhancements, with the following example areas:
  >4 Tx operation
  Enhanced multi-panel/multi-TRP uplink operation
  Frequency-selective precoding
  Further coverage enhancements

## Slide 3
Discussion
Smartphones today are not capable of simultaneously transmitting on more than 2 bands. A high percentage of smartphones is expected to remain so in 2025.
This makes it very difficult for networks to fully exploit all of available uplink resources/bands, and for smartphones to increase their uplink data rates.
The current example areas do not target uplink throughput/capacity enhancements specifically for smartphones:
  Enhancements for >4Tx operation are targeting at devices such as CPEs or IoT devices without size and cost constraints.
  Enhancements for frequency-selective precoding provide most gains when the transmission includes 4 MIMO layers, so such gains would not be applicable for 2Tx smartphones.
  Enhancements for mTRP uplink are in principle applicable to all device types, and provide gains mostly for cell-edge performance in macro-cell mTRP deployments.
  Further coverage enhancements: uplink performance should be improved for smartphones not only in coverage-limited conditions.

## Slide 4
Discussion
Many operators have deployed or plan to deploy NR on more than two frequency bands with different bandwidths, TDD/FDD duplex and DL/UL configurations.
It is necessary to more efficiently utilize all uplink resources in multi-carrier scenarios (>2 bands) where most devices are smartphones with a limited number of Tx antennas (e.g. 2Tx).
UL capability of current commercial NR phones is up to 2 bands UL CA with up to 2Tx simultaneously, with/without Tx switching.
2 UL bands with R17 2Tx switching
2 UL bands CA
Note: PA (Green) is not turned on by RRC config.
Limited number of Tx and power supplies due to complexity, overheating, power limitation, spurious emission and interference.

## Slide 5
Proposal
Include “Enhanced multi-carrier (>2 bands) uplink operation for devices with 2Tx” as an area for Rel-18 uplink enhancements.
2. Uplink enhancements, with the following example areas:
  >4 Tx operation
  Enhanced multi-panel/multi-TRP uplink operation
  Frequency-selective precoding
  Further coverage enhancements
  Enhanced multi-carrier (>2 bands) uplink operation for devices with 2Tx