## Slide 1: Regenerative Architecture for NTN in Rel-18
RP-212214
3GPP TSG RAN #93-e 13-17 September 2021 Online
Source: Ericsson Agenda Item: 9.0.1 Document for: Discussion

## Slide 2: Summary
Status of NTN Architecture discussion after the e-mail discussion (from Moderator’s summary, RP-211658)
NTN Architecture discussions and conclusions of the Rel-16 SI
Additional considerations
Proposed way forward

## Slide 3: Status of NTN Architecture Discussions (from RP-211658)
Listed among the “controversial topics”
Regenerative payload with Inter-Satellite Link:
  “A few companies do not consider Regenerative Payload as necessary to specify in 3GPP as implementation-based solutions are also a possibility. A number of companies would like to treat ISL with Regenerative Payload as backhaul. However, there is not a consensus view if ISL should be considered within the scope of 3GPP depending on the interfaces that are utilized.
  “The moderator recommendation is to have further discussions on this topic at RAN#93-e. At RAN#93-e, the group should consider down-selection to one architecture for regenerative payload from TR 38.821 among gNB, gNB-DU, and IAB-like sat. Follow-on WI objectives based on selected architecture would be further discussed prior to the December Plenary meeting. The down-selection could be accomplished via a Rel-18 SI or decided at RAN Plenary to minimize Rel-18 workload to focus on full gNB based on TR 38.821 findings.”

## Slide 4: NTN Architecture Study in Rel-16 (TR 38.821)
Study and down-selection already took place in Rel-16 and are documented in TR 38.821
  Including conclusions and recommendations
The following architectures for NTN were considered:
  Transparent architecture (adopted for Rel-17)
  Regenerative architecture, gNB on satellite
  Regenerative architecture, gNB-DU on satellite
  Regenerative architecture, relay-like

## Slide 5: Conclusions from the Architecture Study (TR 38.821 Sec. 9.3)
“No showstoppers to support any identified architecture option”, but:
  “In case, the architecture option based on relay-like architecture (IAB) needs to be supported in non-terrestrial networks, further study will be needed.”
  “No specific issues have been identified to support the split regenerative payload case (gNB-DU on board); some protocol adaptation may be needed in a potential normative phase. “
In other words, the only regenerative architecture which can be truly considered applicable “out of the box” is the one with gNB on board

## Slide 6: Additional Considerations (1)
Future scenarios may require even more flexibility, higher data rates for NTN
Xn functionality within the NTN itself is likely to become beneficial
  e.g. Inter-satellite mobility, DC, resource coordination, load management – existing Xn functions can be leveraged
An architecture which enables ISL is arguably more future-proof

## Slide 7: Additional Considerations (2)
gNB on board enables inter-satellite interfaces “out of the box”, gNB-DU on board and IAB-like do not
  Current CU-DU hierarchy precludes an inter-gNB-DU interface
Current CU-DU split in NG-RAN architecture relies on F1, which was not designed to be set up and torn down on the fly
  i.e. there is currently no standards support for gNB-DU to “roam” across gNB-CUs, although implementation-based solutions are not precluded
Implementation-wise, the difference in payload complexity between gNB on board and gNB-DU on board is not expected to be significant
  The main complexity resides in the gNB-DU: carving out the gNB-CU from the payload gives no clear advantage
Similar considerations can be applied to HAPS (see dedicated contribution in RP-212263)

## Slide 8: Proposals
If NTN work is to be approved as part of Rel-18:
  There is no need for further study to down-select the architecture (this was already done in Rel-16 – we should respect the conclusions of TR 38.821)
  Regenerative architecture with gNB on board should be the regenerative architecture of choice

## Slide 9
https://www.ericsson.com/en/5g