## Slide 1: Views on Rel-18 NR MBS Evolution
RP-212246
3GPP TSG RAN WG Meeting #93-e
Electronic Meeting, September 13 - 17, 2021‎
Document for: Discussion
Agenda Item: 9.0.3
China Academy of Telecommunications Technology (CATT)

## Slide 2
From the previous 3GPP RAN discussions [1][2], wide interests on NR MBS evolution in R18 have been expressed by operators, service providers, as well as NW and UE vendors.
  NR MBS is listed as part of the RAN R18 topic list for further discussions on detailed content and scope.
  SA2 discussed on the area as well and their progress has been captured in [3].
This document presents CATT’s view on R18 NR MBS evolution
Background
[1] RWS-210655 Summary of RAN-R18-WS-non-eMBB-Overall
[2] RP-211659 Summary of Evolution for broadcast and multicast services
[3] S2-2106805‎ New SID: Architectural enhancements for 5G multicast-broadcast services Phase ‎‎2‎

## Slide 3: A dedicated WI for NR MBS Enhancements
As per Chair’s guidance in RP-211680, projects will be endorsed after RP#93e meeting, for subsequent RAN discussions toward exact scope for the WIs/SIs
A dedicated Rel-18 WI for NR MBS enhancements is suggested
  The work scope continues new enhancements as well as some continuation based on Rel-17 NR MBS WI
  Less interests observed in the LTE EnTV enhancement discussions
Involved WGs and required TU
  WGs:RAN2 is the leading WG, and impacted WGs included RAN1/3
  TUs:2 TU per meeting in the leading WG (i.e., R2). Such rough estimation is based on a benchmark with what had been spent for R17 NR MBS. The exact numbers can be discussed in a later stage.
Proposal 1: RAN endorse a dedicated project after RP#93e for Rel-18 NR MBS enhancements. It is suggested that 2 TU per meeting in leading WG (i.e., RAN2) is a starting point for further discussions on the potential work scope.

## Slide 4: Overview on potential work scope
We suggest the discussion on potential work scope takes into account the following aspects
  Market requirements
  Specification effort and TU restriction
  Alignment of RAN and SA work scope
We will present our further discussions and views on the main aspects have been discussed in [4], including
  Support for Multicast reception in RRC IDLE/INACTIVE state
  Enhancements to improved support for FTA/ROM
  Enhanced support for SFN
  Improved reliability of PTM (i.e., mainly higher layer aspects based on R17 progress)
  Enhancements for the RAN sharing scenarios
  Power saving enhancements for MBS
[4] RP-211659 Summary of Evolution for broadcast and multicast services

## Slide 5: Support for Multicast reception in INACTIVE/IDLE state
Motivation
    Support of Multicast only in connected state(e.g. per R17 progress by now) can not meet the requirement to support a large number of users, including requirements from SA6 for mission critical services
    To meet the requirement on the balance between power consumption and performance for certain types of devices(e.g. IOT devices)
  Potential work
    Identify and specify enhancements to support multicast reception in IDLE/INACTIVE state, e.g. which delivery mode (i.e., mode 1 or mode 2) to use and how to support such configuration.

## Slide 6: Enhancements for improved support of FTA
Motivation
    Support of FTA is well motivated based on industrial requirement, and there is room for further enhancements based on general broadcast support in Rel-17
    Low standardization effort is expected, i.e., a low hanging fruit to make Rel-18 MBS more promising from industry and business point of view
  Potential work
    Specify necessary enhancements for improved support of Free-To-Air (FTA)/Receive Only Mode (ROM), i.e. including signaling for UE capability report to assist NW configuration of simultaneous reception of FTA / ROM and other services in the serving cells
Proposal 2: ‘Improved support of FTA/ROM’ is included as one objective in the Rel-18 NR MBS WI. Detailed work scope can be further discussed in the subsequent email discussions.

## Slide 7: Enhanced support of SFN
Motivation
    SFN in R17 can not meet the high performance requirements at cell edge, so there is a need to extend it to a larger area
  Potential work
    To study and specify extended CP for SFN support
    To study the potential mechanism to support synchronization across gNBs/DUs for SFN, if needed
  No-SFN performance simulation: Cell edge throughput loss due to interference (3.7Mbps at 10MHz BW)

## Slide 8: Improved reliability of PTM
Motivation
    PTM transmission in R17 can not meet the ultra high reliability requirement from some services(e.g. V2X) and it is not resource efficient to always rely on PTP transmission
      In R17 no conclusion on higher layer reliability support for PTM is reached. This needs to be further studied in R18.
Potential work
    To specify higher layer enhancements for improved reliability of PTM transmission

## Slide 9: Enhancements for the RAN sharing scenarios
Motivation
    Resource efficiency in RAN sharing scenario is not considered in R17 and there is room for improvement.
  Potential work
    Mechanism to improve the resource efficiency for MBS reception in RAN sharing scenarios.
Proposal 3: ‘Resource efficiency improvements for RAN sharing scenarios’ is included as one objective in the Rel-18 NR MBS WI. Detailed work scope can be further discussed in the subsequent email discussions.

## Slide 10: Power saving enhancements for MBS
Discussions and views
    Power saving has been discussed and enhanced in R16/R17 for unicast. Although it is desirable to improve power efficiency for MBS, further studies are needed to better understand its potential benefits and required effort.
    So we propose to include it as a secondary priority objective and it can be included in the Rel-18 work scope if sufficient interests and if time allows.

## Slide 11: Suggested work scope for further discussion
As a summary, our proposals are in the following
Proposal 1: RAN endorse a dedicated project after RP#93e for Rel-18 NR MBS enhancements. It is suggested that 2 TU per meeting in leading WG (i.e., RAN2) is a starting point for further discussions on the potential work scope.
Proposal 2: ‘Improved support of FTA/ROM’ is included as one objective in the Rel-18 NR MBS WI. Detailed work scope can be further discussed in the subsequent email discussions.
Proposal 3: ‘Resource efficiency improvements for RAN sharing scenarios’ is included as one objective in the Rel-18 NR MBS WI. Detailed work scope can be further discussed in the subsequent email discussions.
In [5], we provide WID for R18 NR MBS evolution, as an input to RAN’s further discussions and consolidations of the work scope.
[5] RP-212247, New WID: Enhancements of NR Multicast and Broadcast Services