## Slide 1: Views on US n77 handling
MediaTek Inc.
3GPP TSG RAN 93E RP-212314
September 13th-17th, 2021 Agenda Item 14

## Slide 2: Background
In RP#92e meeting, the following conclusions were achieved. (Proposals 1-4 of section 5.7 in RP-211587)
  RAN4 focuses on the necessary updates to RAN4 requirements and leave signaling work, if any, to RAN2.
  RAN2 focuses on signaling aspects, with an aim to ensure the network can properly deal with legacy n77 UEs that do not support 3.45-3.55 GHz operation in US
  RAN tasks RAN4/2 to complete the required work in Aug. and report back to RAN#93-e
  RAN4 chair is kindly asked to use an appropriate agenda to facilitate the work in Aug. meeting, i.e., R16 maintenance, R16 TEI, etc.
In RAN2#115e meeting
  RAN2 endorsed CRs R2-2109182 to R2-2109185 to add new capability to indicate whether the UE support the extended DoD band in US
  RAN2 suggest adding new NS value to bar legacy UE (LS R2-2109223). But NS value need to be defined by RAN4.
In RAN4#93e meeting
  RAN4 endorsed CR R4-2115112 to modify the NOTE so that it include both C-band and DoD band

## Slide 3: Discussion
[UE capability] UE capability is needed for the network to know whether the UE is capable for 3450-3550MHz in n77. Therefore, the principle in RAN2 CRs is agreeable.
[NS value] NS value can be used to prevent legacy UEs supporting n77 from camping on the DoD bands. However, inputs from US operators are needed to decide whether the NS value is needed.
[CR revision]
  In RAN2 endorsed CR, e.g., R2-2109182, a direct citation to TS38.101-1 is adopted.
  In RAN4 endorsed CR R4-2115112, the 3450-3550MHz is directly added without mentioning the capability
  According to both RAN2 and RAN4 CRs, the UE behavior is clear if extendedBand-n77 is indicated, but may not clear if it is not indicated.
  It is our understanding that absent of extendedBand-n77 but supporting n77 implies that the UE supports C-band only in USA.

## Slide 4: Proposals
Proposal 1: Inputs from US operators are needed to decide whether the NS value is needed.
Proposal 2: Discuss whether a revision of RAN2/RAN4 endorsed CR(s) is needed to clarify the supporting frequency range in n77 while extendedBand-n77 is absent

## Slide 5: Thank You!