## Slide 1
Joint Proposal on Fast role change in CA/DC
3GPP TSG RAN Meeting #93e
Electronic Meeting, September 13 – 17, 2021
Source: ZTE, Sanechips, Samsung, Verizon
Agenda: 9.0.3
RP-212391

## Slide 2: Motivation - Fast role change
For the case of CA/DC, especially for the FR1+FR1 or FR2+FR2 CA/DC, in case radio conditions in PCell/MCG becomes poor, RRC reestablishment is triggered to recover the PCell/MCG even if the Scell/SCG is in perfectly good radio conditions
  RRC Reestablishment results in significant interruption time for the user plane
  A fast role change procedure (i.e. change the SCell/SCG to PCell/MCG) can be used to avoid this interruption time
Limitations in current specifications:
  Changing the SCell/SCG to PCell/MCG, even if the connection in SCell/SCG is good requires SCell/SCG to be released and the NW needs to configure the new PCell/MCG based on the configuration of previous SCell/SCG
  The existing procedure results in following problems:
    unnecessary interruption time due to delay caused by F1/E1/Xn inter-node interaction and RACH procedure in air interface) and
    Extra signaling overhead (Since SCell/SCG will be released and the same cell has to be configured as PCell/MCG)

## Slide 3: Enhancement - Fast Role Change
To reduce the interruption time and improve the user experience, we propose to support fast role change for CA/DC in Rel-18 and the scope can as follows:
Support fast role change between SCell and PCell in CA case, and fast role change between MCG and SCG in DC case:
  The SCell/SCG configuration release/addition shall be avoided in role change [RAN2, RAN3]
  The inter-node interaction (e.g. F1/E1/Xn) for role change shall be minimized [RAN3, RAN2]
  Unnecessary RACH procedure should be avoided during the role change procedure [RAN2]
  Both UE triggered role change (e.g. in failure case), and NW triggered role change shall be considered [RAN2, RAN1?]
  Prioritize the fast role change without security key refresh [RAN2]

## Slide 4: Thanks