## Slide 1
3GPP TSG RAN Meeting #93e RP-212450
Electronic Meeting, September 13-17, 2021
Agenda item : 9.0.2
Source : Samsung
Title : View on the scope of Rel-18 UL MIMO for NR
Document for : Discussion and Decision

## Slide 2: Background | Latest categorization for DL MIMO and UL [RWS-210659] (RAN1 led)
1. Evolution for downlink MIMO, with the following example areas:
  Further enhancements for CSI (e.g., mobility, overhead, etc.)
  Evolved handling of multi-TRP (Transmission Reception Points) and multi-beam
  CPE(customer premises equipment)-specific considerations
2. Uplink enhancements, with the following example areas:
  >4 Tx operation
  Enhanced multi-panel/multi-TRP uplink operation
  Frequency-selective precoding
  Further coverage enhancements
The contribution will focus on MIMO-related aspects of item 2 (uplink enhancements)

## Slide 3: Background |Outcome of email discussion – UL MIMO
Uplink enhancements, with the following skeleton of the possible objectives:
  Study and if necessary specify >4 Tx UL operation, e.g., for CPE/FWA/vehicle/Industrial devices [leading WG: RAN1]
  Specify enhanced multi-panel uplink operation and/or enhanced multi-TRP uplink operation, potentially including fast UL panel selection, separate UL timings/power controls for different panel/TRP and/or simultaneous multi-panel UL transmission [leading WG: RAN1]
  Study and if necessary specify frequency-selective precoding, mainly targeting devices with >=4 Tx [leading WG: RAN1]
  Specify further coverage enhancements including PRACH enhancement for FR2 e.g., PRACH repetition with same or different beams [leading WG: RAN1]
  Study and if necessary specify power domain enhancements e.g., dynamic power aggregation [leading WG: RAN4 or RAN1]
  Potentially specify other UL enhancements e.g., enhancement for multi-carrier UL operation, enhancements for DFTS-OFDM, enhancement for UL CW mapping [leading WG: RAN1]
For >4 Tx UL operation,
  FFS: whether only some listed example device types are targeted or even other device types are also targeted
  FFS: target frequency range
  FFS: RAN4 as secondary WG
For enhanced multi-panel uplink operation and/or enhanced multi-TRP uplink operation,
  FFS: further clarification and narrowing down of the scope for this example area based on listed example scopes as starting point
  FFS: enhancements are based on Rel-17 unified TCI framework
  FFS: target frequency range
  FFS: RAN2/4 as secondary WG
For frequency-selective precoding,
  FFS: whether this example area can be generalized to enhanced uplink precoding
  FFS: target frequency range and target devices
  FFS: RAN4 as secondary WG
For further coverage enhancement and power domain enhancement
  FFS: further clarification and narrowing down of the scope for this example area based on listed example scopes as starting point
  FFS: other coverage enhancement e.g., DMRS-less PUCCH
For other potential UL enhancements
  FFS: further clarification and narrowing down of the scope for this example area based on listed example scopes as starting point
  FFS: other potential scope, e.g., enhancement for UL dense deployment
Non-controversial
Controversial

## Slide 4: Assessment on conclusion of email discussion | Example area 1
Example Area 1: >4Tx UL operation
[Non-controversial]
  Study and if necessary specify >4 Tx UL operation, e.g., for CPE/FWA/vehicle/Industrial devices [leading WG: RAN1]
[Controversial]
  FFS: whether only some listed example device types are targeted or even other device types are also targeted
  FFS: target frequency range
  FFS: RAN4 as secondary WG
#1: Agree that study phase is needed before committing to specification work, study includes
  Codebook-based (including >4Tx codebook design) and non-codebook based UL transmission
  RS (>4 port SRS resource, DMR for > 4 layers)
  Other Rel. 18 (e.g. example area 2 and 3) for >4Tx operations
#2: Antenna structure, channel model, and scenario
  Uniform, dual-polarized can be assumed for CPE/FWA/vehicle/Industrial devices
  Including both single and multi-panels
  Channel model and scenarios needs to be discussed for the study
#3: Items labelled [Controversial]
  1st FFS: devices with feasible >4Tx operation should be prioritized
  2nd FFS: both FR1 and FR2, and including multi-panel UE
  3rd FFS: RAN4 as secondary WG can be discussed later when the scope is more clear

## Slide 5: Assessment on conclusion of email discussion | Example area 2
Example Area 2: enhanced multi-panel uplink operation and/or enhanced multi-TRP uplink operation
[Non-controversial]
  Specify enhanced multi-panel uplink operation and/or enhanced multi-TRP uplink operation, potentially including fast UL panel selection, separate UL timings/power controls for different panel/TRP and/or simultaneous multi-panel UL transmission [leading WG: RAN1]
[Controversial]
  FFS: further clarification and narrowing down of the scope for this example area based on listed example scopes as starting point
  FFS: enhancements are based on Rel-17 unified TCI framework
  FFS: target frequency range
  FFS: RAN2/4 as secondary WG
#1: Agree with the specification work, at least for some aspects, since
  Basic signaling support for multi-panel UE (assuming some support in Rel.17) still is quite limited for simultaneous UL transmission
#2: Potential enhancements should be based on (or a continuation) of Rel.17 work, including
  Baseline from the support for indication of N>1 UL TCI states based on (potential) Rel-18 DL MIMO enhancements on unified TCI framework
  Per TRP UL control parameters such as TA, UL PC need some study on potential benefits before committing on specification (depending on target use cases, e.g. whether dense UL is agreed or not, whether multiple TA is needed given UL synchronization requirements)
#3: Items labelled [Controversial]
  1st FFS: the scope with potential narrowing down or example of enhancements can be discussed
  2nd FFS: this enhancement should be based on Rel.17 unified TCI and multi-TRP frameworks
  3rd FFS: both FR1 and FR2
  4th FFS: agree with RAN2 as secondary WG, and RAN4 as another WG can be discussed after scope becomes clear

## Slide 6: Assessment on conclusion of email discussion | Example area 3
Example Area 3: frequency selective precoding
[Non-controversial]
  Study and if necessary specify frequency-selective precoding, mainly targeting devices with >=4 Tx [leading WG: RAN1]
[Controversial]
  FFS: whether this example area can be generalized to enhanced uplink precoding
  FFS: target frequency range and target devices
  FFS: RAN4 as secondary WG
#1: Agree that study phase is needed before committing to specification work
  Objective of the study needs to be clearly stated, i.e., study the benefits considering DL control overhead (i.e. performance vs DL overhead tradeoff)
#2: Scope of study and potential enhancements (if found beneficial)
  Codebook enhancement for both 4Tx and >4Tx, including dual-stage codebook
  DL control signaling for overhead reduction, including two-stage DCI
#3: Items labelled [Controversial]
  1st FFS: scope of study should be clear, i.e. frequency selective precoding; it is unclear what generalized UL precoding means
  2nd FFS: both FR1 and FR2
  3rd FFS: RAN4 as secondary WG can be discussed later when the scope is more clear

## Slide 7: Assessment on conclusion of email discussion | Other
[Non-controversial]
  Potentially specify other UL enhancements e.g., enhancement for multi-carrier UL operation, enhancements for DFTS-OFDM, enhancement for UL CW mapping [leading WG: RAN1]
[Controversial]
  FFS: further clarification and narrowing down of the scope for this example area based on listed example scopes as starting point
  FFS: other potential scope, e.g., enhancement for UL dense deployment
#1: Do not support the specification work
  Multi-carrier UL operation: needs clarification about the main use case and key differences w.r.t. Rel-16/17
  Enhancements for DFTS-OFDM: no need and unclear benefits
    for low PAPR (coverage limited), rank>1 is unlikely
    gNB complexity of DFTS-OFDM MIMO (link adaptation, MIMO RX)
    we can use rank=1 CP-OFDM and rank>1 CP-OFDM
  UL CW mapping:
    benefits need to be justified via proper study (cf. during RAN15, no benefits were observed)
    Unclear whether it is for <= 4 layers or also for > 4 layers (if >4Tx operation is supported)
#2: Items labelled [Controversial]
  1st FFS: agree with the need for clear scope for further discussion
  2nd FFS: the use case of UL dense deployment is clear, hence can be discussed

## Slide 8: Proposal |
On Rel-18 UL MIMO enhancement, include example areas 1, 2 and 3 from the moderator conclusion with the following refinement (in red)
  Area 1: scope of study should be clear
    Study and if necessary specify >4 Tx UL operation, e.g., for CPE/FWA/vehicle/Industrial devices, and including enhancements on CB-based, non-CB-based, RS, and other Rel.18 enhancements (area 2 and 3) [leading WG: RAN1]
  Area 2: this enhancement will build on Rel. 17 foundational features
    Based on the Rel.17 unified TCI and multi-TRP frameworks,
      Specify enhanced multi-panel uplink operation and/or enhanced multi-TRP uplink operation, potentially including fast UL panel selection,
      Study and if necessary specify separate UL timings/power control for different panel/TRP and/or simultaneous multi-panel UL transmission [leading WG; RAN1]
  Area 3: objective of the study should be clearly stated
    Study and if necessary specify frequency-selective precoding, mainly targeting devices with >=4 Tx, based on performance vs DL control overhead tradeoff, and including codebook enhancements and DL control signaling design [leading WG: RAN1]