## Slide 1: Moderator's summary for discussion on [RAN94e-R18Prep-03] Additional topological improvements - smart repeater
RAN1 Chair (Samsung)
3GPP TSG-RAN Meeting #94-e
Electronic Meeting, December 6-17, 2021
Agenda Item: 8A.1
RP-212663

## Slide 2: Proposals (1/2)
Proposal 1 (should be agreeable): For smart repeaters, start with study item.
Proposal 2 (non-controversial): For smart repeaters, RAN1 is the primary working group. Secondary working groups are RAN2, RAN3, and RAN4.
Proposal 3 (should be agreeable): Study and identify which side control information is necessary for smart repeaters including at least [RAN1, RAN2, RAN4]
  Beamforming information
  Timing information to align transmission / reception boundaries of smart repeater
  Information on UL-DL TDD configuration
  Power control information for efficient interference management
  ON-OFF information for efficient interference management and improved energy efficiency

## Slide 3: Proposals (2/2)
Proposal 4 (should be agreeable): Study the following aspect of smart repeater
  Identification and authorization of smart repeaters [RAN2, RAN3]
  RF requirements for smart repeater, including max transmission power and other applicable RF requirements [RAN4]
Proposal 5 (should be agreeable): Focus Rel-18 smart repeater work on the following scenario / assumptions:
  Consider smart repeaters used for extension of network coverage on FR1 and FR2 bands. Prioritize FR2 TDD deployments for both outdoor and O2I scenarios.
  For only single hop stationary smart repeaters
  Assuming smart repeaters are transparent to UEs
  Smart repeater can maintain the gNB-repeater link and repeater-UE link simultaneously
  Cost efficiency is a key consideration point for smart repeaters